Ceiling Diffuser Model 4-DF

Specification texts

Ceiling diffuser type 4DF for supply and return air, horizontal throw in 4 directions. Particularly suitable for installation in comfort rooms with high number of air changes, for clean rooms (in connection with particle filter boxes) and for VAV installations with variable volumetric flows (between 40-100%).

Consisting of square sheet steel faceplate painted with a high-quality powder coating to a RAL colour (RAL 9010, white, standard), with integrated fixed air deflection blades, with concealed mounting (VM). For use in isothermal mode and in cooling mode (up to -14 K) and a room height of 2 - 4.5 m. Sophisticated design allows easy cleaning to VDI 6022.

Product: SCHAKO type 4DF-...

-	Faceplate made of natural colour anodised aluminium (E6/EV1) (only available with concealed mounting)

-	with screw mounting (-SM), only for connection to fire protection unit.

Accessories:

-	Plenum box (SK-Q-...) made of galvanised sheet steel, with fixing lugs (only available in conjunction with concealed mounting) (-Z).

-	Supply air model with integrated perforated straightener (-A).

-	Return air model without perforated straightener.

-	with damper (-DK1/-DK2) in plenum box, adjustable from below, for simple air volume regulation without dismounting the faceplate.

-	with damper without cable-operated adjustment (-DK1)

-	with damper with cable-operated adjustment (-DK2)

-	with volumetric flow meter (-VME1).

-	with ROB model (-ROB1), removable diffuser plate, damper and volumetric flow meter.

-	with rubber lip seal (-GD1), on plenum box spigot, made of special rubber.

-	with thermal insulation

-	internal (-Ii)

-	external (-Ia)

-	height of plenum box can be freely selected, xxx in mm, (heightmin = spigot diameter + 102 mm, but at least 200 mm) (For models SK-Q-07-Z-310 / -400-...-DK1/-DK2-...-S0, observe special height of plenum box (see p. 5))

-	Spigot diameter can be freely selected, xxx in mm

-	Spigot position

-	S0 = spigot from above

-	S1 = 1 lateral spigot on the box (standard)

-	S2 = 2 spigots offset by 90°

-	S3 = 2 spigots offset by 180°

-	S5 = 2 spigots arranged next to each other