Ventilation grille AL

Specification Text

Ventilation grille type AL-... for supply and return air, for installation in rectangular ducts or plenum boxes. With front side horizontal or vertical, pivoting, individually adjustable air deflection blades. For description of frames and blades, see “Material / paint”. Assembly parts made of electrolytically galvanised sheet steel.

Product: SCHAKO type AL-…

Blades:

-	horizontal pivoting air deflection blades on the front side (-01).

-	same as AL-01-…, additionally with vertical, pivoting air de-flection blades (-02).

-	same as AL-01-…, additionally with hit-and-miss damper (-05).

-	same as AL-01-…, additionally with vertical pivoting air de-flection blades and hit-and-miss damper (-06).

-	vertical, pivoting air deflection blades on the front side (-11).

-	same as AL-11-…, additionally with horizontal, pivoting air deflection blades (-12).

-	same as AL-11-…, additionally with hit-and-miss damper (-15).

-	same as AL-11-…, additionally with horizontal pivoting air deflection blades and hit-and-miss damper (-16).

Length and single / band design:

Single design (-N) (standard):

-	325 mm (-N-00325)

-	425 mm (-N-00425)

-	525 mm (-N-00525)

-	625 mm (-N-00625)

-	825 mm (-N-00825)

-	1025 mm (-N-01025)

-	1225 mm (-N-01225)

Band design (-B) (only possible for AL-11 / AL-12 / AL-15 / AL-16):

-	length in mm, freely selectable (-B-xxxxx), for band de-sign (for a grille length BL > 1225 mm: 2-part for a length of band BL ≤ 2424 mm, multi-part for a length of band > 2424 mm, module length max. 1225 mm) (always with 5 digits).

Height:

-	75 mm (-075)

-	125 mm (-125)

-	225 mm (-225)

-	325 mm (-325)

Material / paint (faceplate):

-	Aluminium (-AL-…)

-	natural colour anodised (E6/EV1, only possible with concealed mounting (-ELOX) (standard).

-	painted to a RAL colour of your choice, freely selectable (-xxxx-…, at an extra charge).

Mounting:

-	screw mounting (-SM, standard for band design)

-	screws must be provided on site.

-	concealed mounting (-VM, standard, only possible with a plenum box or an installation frame).

-	clamp mounting (-KB, standard for model without plenum box and without installation frame).

Accessories:

-	Plenum box (AK-33), in rectangular design, made of galvanised sheet steel (-SV, standard), housing with round connection spigot and mounting brackets.

-	Length:

-	325 mm (-00325)

-	425 mm (-00425)

-	525 mm (-00525)

-	625 mm (-00625)

-	825 mm (-00825)

-	1025 mm (-01025)

-	1225 mm (-01225)

-	length in mm, freely selectable (-xxxxx), for band design (for a grille length BL > 1225 mm: 2-part for a length of band BL ≤ 2424 mm, multi-part for a length of band > 2424 mm) (always with 5 digits).

-	Height:

-	75 mm (-075)

-	125 mm (-125)

-	225 mm (-225)

-	325 mm (-325)

-	Single / band design:

-	Single design (-N) (standard).

-	band design (-B) (only possible for AL-11 / AL-12 / AL-15 / AL-16, for a grille length BL > 1225 mm, available lengths according to SCHAKO standard for band de-sign).

-	Mounting:

-	screw mounting (-SM) (standard for band design, screws must be provided on site).

-	concealed mounting (-VM) (standard for single de-sign).

-	Damper:

-	without damper (-DK0) (standard).

-	with damper (-DK1), made of galvanised sheet steel, in the plenum box housing, adjustable, for simple air volume regulation, standard with lateral spigot position (-S1).

-	with damper (-DK2), same as DK1, but with cable-operated adjustment, standard with spigot position from above (-S0) and front side spigot position (-S4).

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.

-	Insulation:

-	without insulation (-I0) (standard).

-	with internal insulation (-Ii), thermal insulation in-side the plenum box.

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS).

-	height of plenum box in mm, freely selectable (-xxx) (minimum height [KHS] with spigot position -S1 and -S4 = spigot diameter +87 mm, but at least 200 mm) (always with 3 digits).

-	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	spigot diameter in mm, freely selectable (-xxx, al-ways with 3 digits) (with spigot positions -S0 and -S4, if the spigot diameter is increased, only the off-set plenum box shape is available).

-	Spigot position:

-	Spigot from above (-S0).

-	Lateral spigot on the plenum box (-S1) (standard).

-	Front side spigot (-S4) (not possible for band de-sign).

-	Installation frame (-ER0 / -ER1 / -ER2)

-	without installation frame (-ER0).

-	with installation frame made of galvanised sheet steel (only possible in the absence of a plenum box):

-	without wall anchors (-ER1).

-	with wall anchors (-ER2).