Weather Protection Grille Model ALA-SO

Specification texts

External air intake grille type ALA-SO especially designed for small construction sizes, with fixed rain-repellent blades and back-fitted wire mesh. Frame and blades made of anodised natural colour aluminium profiles (E6/EV1). Wire mesh grid made of galvanised sheet steel.

Product: SCHAKO type ALA-SO

Accessories:

-	Mounting frame (-E1) made of electrolytically galvanised sheet steel, perforated (unperforated if pre-ordered)