Fan Coil Unit Aquaris Silent

Specification text

High-efficiency fan convector Aquaris Silent for horizontal or vertical installation in false ceilings, cavity floors, walls or free-standing/freely suspended with casing. The housing of the device consists of profiles and covers made of galvanized sheet steel and provided with polyethylene heat and sound insulation with a thickness of 6 mm. The energy-efficient EC motor fan consists of double-sided intake-operated centrifu-gal blower with direct drive. The 2-pipe or 4-pipe heat ex-changers or registers have a rack made of galvanized steel, aluminum ribs and copper pipes. With condensate pan according to VDI 6022 made of stainless-steel sheet. Filter efficiency ISO Coarse < 40%. It consists of synthetic fabric on a plastic frame.

Product:	SCHAKO

Family: 	fan convector Aquaris Silent

Aquaris Silent models

Type

Fan convector Aquaris Silent	-AQS

Motor

EC motor		-EC

Size

Size 1 		-1

Size 2 		-2

Size 3 		-3

Size 4 		-4

Size 5 		-5

System (water register version)

2-pipe register 1 row of pipes (heating)	-R1

2-pipe register 3 rows of pipes (cooling or heating)	-R3

4-pipe register 1 and 3 pipe rows (heating and cooling)	-L4

Air filter

ISO Coarse <40 %	-C1

ISO Coarse 40 %	-C4

Mounting

horizontal – ceiling	-H

horizontal – floor	-B

vertical – wall	-V

Intake position

secondary air intake, straight	-1

Duct connection

without flange	-F0

with supply air flange	-FZ

Water connection position

water connection in air flow direction on the left	-W1

water connection in air flow direction on the right	-W2

Cooling valve

without cooling valve, without pipe set, without shut-off valve	-00

cooling valve VPP46.10L0.2 with pipe set and shut-off valve	-01

cooling valve VPP46.10L0.4 with pipe set and shut-off valve	-02

cooling valve VPP46.15L0.2 with pipe set and shut-off valve	-03

cooling valve VPP46.15L0.6 with pipe set and shut-off valve	-04

cooling valve VPP46.20F1.4 with pipe set and shut-off valve	-05

cooling valve AB-QM-003Z8221 with pipe set and shut-off valve	-25

cooling valve AB-QM-003Z8220 with pipe set and shut-off valve	-26

cooling valve AB-QM-003Z8222 with pipe set and shut-off valve	-27

cooling valve AB-QM-003Z8223 with pipe set and shut-off valve	-31

Heating valve

without heating valve, without pipe set, without shut-off valve	-00

heating valve VPP46.10L0.2 with pipe set and shut-off valve	-01

heating valve VPP46.10L0.4 with pipe set and shut-off valve	-02

heating valve VPP46.15L0.2 with pipe set and shut-off valve	-03

heating valve VPP46.15L0.6 with pipe set and shut-off valve	-04

heating valve VPP46.20F1.4 with pipe set and shut-off valve	-05

heating valve AB-QM-003Z8221 with pipe set and shut-off valve	-25

heating valve AB-QM-003Z8220 with pipe set and shut-off valve	-26

heating valve AB-QM-003Z8222 with pipe set and shut-off valve	-27

heating valve AB-QM-003Z8223 with pipe set and shut-off valve	-31

Actuator

without actuator	-000

with thermal actuator SAST127474	-T01

with thermal actuator SAST127475	-T02

with thermal actuator SAPV127957	-T03

with thermal actuator SAPV128561	-T04

with thermal actuator SAPO129150	-T05

with motorised actuator SMPV132351	-M01

with motorised actuator SMPO132353	-M02

with motorised actuator SMPO132352	-M03

Position of electrical connection

electrical connection in air flow direction on the left	-S1

electrical connection in air flow direction on the right	-S2

with offset electrical connection box in air flow direction on the left 1.5 m	-S3

with offset electrical connection box in air flow direction on the right 1.5 m	-S4

Additional control and regulation elements

without additional control and regulation elements	-0

with fault message output	-1

with EC interface for 3-stage controller	-2

Valve condensate pan

without valve condensate pan	-K0

with valve condensate pan on the side of the hydraulic connection	-KH

Condensate pump

without condensate pump	-0

with condensate pump Si-10, mounted ex works	-1

Flexible connection models

Type

Flexible connection	-FA

Family

for fan convector Aquaris Silent	-AQS

Model

standard product	-000

Size

Size 1 		-1

Size 2 		-2

Size 3 		-3

Size 4 		-4

Size 5 		-5

Model

150 mm for supply air	-Z1

290 mm for supply air	-Z2

150 mm for return air	-A1

290 mm for return air	-A2

Models of frame for mineral/glass wool air duct

Type

frame for mineral/glass wool air duct	-FW

Family

for fan convector Aquaris Silent	-AQS

Size

Size 1 		-1

Size 2 		-2

Size 3 		-3

Size 4 		-4

Size 5 		-5

Model

for supply air	-Z

for return air	-A

Plenum box models

Type

plenum box	-PL

Family

for fan convector Aquaris Silent	-AQS

Model

standard product	-000

Size

size 1 = 720 mm	-1

size 2 = 935 mm	-2

size 3 = 1270 mm	-3

size 4 = 1375 mm	-4

size 5 = 1620 mm	-5

Model

supply air box	-Z

return air box	-A

Length

L = 200 mm	-0200

L = 300 mm	-0300

L = 400 mm	-0400

L = 500 mm	-0500

L = 600 mm	-0600

L = 700 mm	-0700

L = 800 mm	-0800

L = 900 mm	-0900

L = 1000 mm	-1000

L = 1100 mm	-1100

length in mm	-xxxx

Insulation

without insulation	-I0

thermal insulation of 10 mm	-I1

sound and thermal insulation of 20 mm	-I2

sound and thermal insulation of 40 mm	-I4

Connection in air flow direction

closed in air flow direction	-M00

open in air flow direction	-MAB

connecting flange in air flow direction	-MRE

with x spigot DN123 in air flow direction	-M1x

with x spigot DN158 in air flow direction	-M2x

with x spigot DN158 in air flow direction	-M3x

Connection in air flow direction on the left

without spigot in air flow direction on the left	-L00

with x spigot DN123 in air flow direction on the left	-L1x

with x spigot DN158 in air flow direction on the left	-L2x

with x spigot DN198 in air flow direction on the left	-L3x

Connection in air flow direction on the right

without spigot in air flow direction on the right	-R00

with x spigot DN123 in air flow direction on the right	-R1x

with x spigot DN158 in air flow direction on the right	-R2x

with x spigot DN198 in air flow direction on the right	-R3x

Models of transition piece for air diffuser

Type

transition piece for air diffuser	-US

Family

for fan convector Aquaris Silent	-AQS

Size

Size 1 		-1

Size 2 		-2

Size 3 		-3

Size 4 		-4

Size 5 		-5

Model

for supply air	-Z

Length

length L = xxxx mm	-xxxx

Fan convector position

fan convector centered	-M

fan convector offset to the right	-R

fan convector offset to the left	-L

Insulation

without insulation	-I0

thermal insulation of 10 mm	-I1

Air flow direction

intake straight	-1

Air diffuser

with ceiling air diffuser DBB	-D1

with ventilation grille IB-Q	-R1

Air diffuser colour

white like RAL 9010	-22

colour of air diffuser xy according to table on page 19	-xy

Mounting

visible mounting	-SM

concealed mounting	-VM

Primary air connection spigot

Without primary air connection spigot	-P0

Primary air spigot diameter

Without primary air connection spigot	-0

Device casing models

Type

device casing	-GV

Family

for fan convector Aquaris Silent	-AQS

Size

Size 1 		-1

Size 2 		-2

Size 3 		-3

Size 4 		-4

Size 5 		-5

Mounting

horizontal – ceiling	-H

vertical – wall	-V

Secondary air grille

with secondary air open	-R0

with secondary air closed without grille	-R1

with secondary air DBB	-R2

with secondary air PA	-R3

Colour

black colour like RAL 9005	-1

white colour like RAL 9010	-2

white colour like RAL 9016	-3

grey colour like RAL 9006	-4

Mounting kit

with mounting kit	-M0

without mounting kit	-M1

Models of accessories supplied loose

Flexible hydraulic connection

EDE-13 500 mm	-1

EDE-13 800 mm	-2

EDE-13 1200 mm	-3

AG male thread 1/2	-A

AG male thread 3/4	-B

ÜMF flat seal spigot nut 1/2	-C

ÜMF flat seal spigot nut 3/4	-D

R-AG-D rotating male thread 1/2	-E

R-AG-D rotating male thread 3/4	-F

Shut-off valve

STH BOSTON 31038 1/2	-VE01

Pressure-independent control valve

VPP46.10L0.2, G1/2	-VC01

VPP46.10L0.4, G1/2	-VC02

VPP46.15L0.2, G 3/4	-VC03

VPP46.15L0.6, G 3/4	-VC04

VPP46.20F1.4, G 1	-VC05

AB-QM-003Z8221, DN 15, G 3/4 A	-VC25

AB-QM-003Z8220, DN 15, G 3/4 A, LF	-VC26

AB-QM-003Z8222, DN 15, G 3/4 A, HF	-VC27

AB-QM-003Z8223, DN 20, G 1 A	-VC31

AB-QM-003Z8224, DN 20, G 1 A, HF	-VC32

6-way ball valve

VWG41.10-0.25-0.4, G 1/2	-V601

VWG41.10-0.25-0.65, G 1/2	-V602

VWG41.10-0.25-1.0, G 1/2	-V603

VWG41.10-0.4-0.65, G 1/2	-V604

VWG41.10-0.4-1.0, G 1/2	-V605

VWG41.10-0.4-1.3, G 1/2	-V606

VWG41.10-0.4-1.6, G 1/2	-V607

VWG41.10-0.65-1.0, G 1/2	-V608

VWG41.10-0.65-1.3, G 1/2	-V609

VWG41.10-0.65-1.6, G 1/2	-V610

VWG41.10-1.0-1.3, G 1/2	-V611

VWG41.10-1.0-1.6, G 1/2	-V612

VWG41.10-1.0-1.9, G 1/2	-V613

VWG41.10-1.3-1.6, G 1/2	-V614

VWG41.10-1.3-1.9, G 1/2	-V615

VWG41.10-1.6-1.9, G 1/2	-V616

VWG41.10-1.9-1.9, G 1/2	-V617

VWG41.10-0.25-1.3, G 1/2	-V618

VWG41.10-0.25-1.6, G 1/2	-V619

VWG41.10-0.25-1.9, G 1/2	-V620

VWG41.10-0.4-0.4, G 1/2	-V621

VWG41.10-0.4-1.9, G 1/2	-V622

VWG41.10-0.65-0.65, G 1/2	-V623

VWG41.10-0.65-1.9, G 1/2	-V624

VWG41.10-1.0-1.0, G 1/2	-V625

VWG41.10-1.3-1.3, G 1/2	-V626

VWG41.10-1.6-1.6, G 1/2	-V627

VWG41.20-0.65-2.5, G 1	-V628

VWG41.20-1.0-2.5, G 1	-V629

VWG41.20-1.6-2.5, G 1	-V630

VWG41.20-1.6-3.45, G 1	-V631

VWG41.20-2.5-3.45, G 1	-V632

VWG41.20-2.5-4.25, G 1	-V633

VWG41.20-4.25-4.25, G 1	-V634

VWG41.20-0.25-2.5, G 1	-V635

VWG41.20-0.25-3.45, G 1	-V636

VWG41.20-0.25-4.25, G 1	-V637

VWG41.20-0.4-2.5, G 1	-V638

VWG41.20-0.4-3.45, G 1	-V639

VWG41.20-0.4-4.25, G 1	-V640

VWG41.20-0.65-3.45, G 1	-V641

VWG41.20-0.65-4.25, G 1	-V642

VWG41.20-1.0-3.45, G 1	-V643

VWG41.20-1.0-4.25, G 1	-V644

VWG41.20-1.3-2.5, G 1	-V645

VWG41.20-1.3-3.45, G 1	-V646

VWG41.20-1.3-4.25, G 1	-V647

VWG41.20-1.6-4.25, G 1	-V648

VWG41.20-2.5-2.5, G 1	-V649

VWG41.20-3.45-3.45, G 1	-V650

Valve adapter

ALG132, female thread G 1/2 to male thread R 3/8	-VA01

ALG142, female thread G 3/4 to male thread R 1/2 	-VA02

Thermal actuator

SAST127474, ON/OFF, 230 V AC	-AT01

SAST127475, ON/OFF, 24 V AC/DC	-AT02

SAPV127957, 0-10 V, 24 V AC, + valve travel detection	-AT03

SAPV128561, 0-10 V, 24 V DC, + valve travel detection	-AT04

SAPO129150, 0-10 V, 24 V AC/DC, + valve travel detection + feedback signal	-AT05

Motorised actuator

SMPV132351, 0-10 V, 24 V AC/DC, + valve travel detection	-AM01

SMPO132353, 0-10 V, 24 V AC/DC, + valve travel detection + feedback signal	-AM02

SMPO132352, 0-10 V, 24 V AC/DC, + valve travel detection + feedback signal	-AM03

6-way ball valve

GDB341.9E, 3P, 230 V AC	-AR01

GDB161.9E, 0-10 V, 24 V AC/DC	-AR02

GDB111.9E, KNX, 24 V AC	-AR03

Room thermostat

RDG160T	-TR05

Room thermostat with KNX interface

RDG160KN	-TK02

RDG260KN	-TK04

Condensate pump

Si-10			-KK01

Mounting kits

mounting kit for device casing GV-AQS	-MGV1

Pipe sets

pipe set for 2-pipe register 1 pipe row left	-RR11

pipe set for 2-pipe register 1 pipe row right	-RR12

pipe set for 2-pipe register 3 pipe rows left	-RR31

pipe set for 2-pipe register 3 pipe rows right	-RR32

pipe set for 4-pipe register 1 and 3 pipe rows left	-RL41

pipe set for 4-pipe register 1 and 3 pipe rows right	-RL42