Compact Air-Conditioning Module Model Aquaris KWB

Specification texts

Plug-in compact air-conditioning module for offices for installation in corridor false ceilings for unilateral air intake and evacuation, observing stringent requirements of air throw and sound. Filter easy to replace without requiring special tools. Control via 3-speed switch or by means of room temperature sensor, depending on room temperature.

Product: SCHAKO type Aquaris KWB-...-

- 	Model:

-	10...

-	20...

-	Heat exchanger:

- 2-pipe (-2)

- 4-pipe (-4)

-	Electric connection:

-	left

-	right

-	Water connection:

-	left (-L)

-	right (-R)

-	Condensate connection:

-	left

-	right

Accessories:

-	Valves for water-side control of air after-treatment devices in closed circuits

-	Three-way valve with T-bypass having a nominal pressure of 16 bar. Red brass housing.

External thread connections G...B. Type VMP 46...

-	Room operating unit

-	Two-point controller for heating and/or cooling systems

-	Other control versions available on request

-	Relay kit for disconnecting up to 5 Aquaris Silent operated in parallel on one control unit.

-	Valve condensate pan made of galvanised sheet steel for discharging the condensate formed in the valve into the drain channel.

-	Condensate pump for removing the water of condensation from the cooling register, in case there is not enough gradient towards the on-site drain system. Equipped with an overflow alarm contact (8 A/250 V) when the water height rises above 27 mm.