Air Diffuser System Model AUDIX-AW

Specification texts

Air diffuser system for supply air, with rectangular connection pipe, with integrated silencer for installation in front of lightweight walls for connection of 1 diffuser. Plenum box made of galvanised sheet steel. Integrated silencer to prevent cross-talk sound and for silencing in the duct consisting of an abrasion-resistant absorption material laid out as reverse labyrinth and attached on both sides, including a fitting system to assemble it outside the columns of lightweight walls.

Product: SCHAKO Type AUDIXÒ-AW-RE-Z

-	Air diffuser system for return air

Product: SCHAKO Type AUDIXÒ-AW-RE-A

-	Air diffuser system for supply and return air

Product: SCHAKO Type AUDIXÒ-AW-RE-Z/A

-	Air diffuser system for return air, with round connection pipe, with integrated silencer for installation in front of lightweight walls to connect 1 diffuser.

Product: SCHAKO type AUDIXÒ-AW-R-Z

-	Air pass system for return air, with round spigot, with integrated silencer for installation in front of lightweight walls for connection of 1 diffuser.

Product: SCHAKO type AUDIXÒ-AW-R-A

-	Air diffuser system for supply and return air, with round connection pipe, with integrated silencer for installation in front of lightweight walls to connect 1 diffuser.

Product: SCHAKO type AUDIXÒ-AW-R-Z/A

Equipped with:

Diffuser type: ................ from SCHAKO for subsequent final assembly, with concealed fixing via springs.

Simple assembly and disassembly for maintenance purposes

Diffusers:

-	DSA-1: 1 row

-	Sheet steel faceplate painted to RAL 9005 (black) or RAL 9010 (white)

-	Plastic nozzles, similar to RAL colour 9005 (black, standard) or RAL 9010 (white)

-	Fixed (-D) or adjustable (-VD) nozzles

-	with spring connection (-FM)

Product: SCHAKO Type DSA-1

-	DSC40..: 1 or 2 slots

-	Frame profile made of aluminium natural colour anodised (E6/EV1) or aluminium painted to RAL 9010 (white)

-	Pivoting air deflection blades in support blade profiles made of plastic (hard PVC)

- 	similar to RAL colour 9005 (black)

-	similar to RAL colour 9010 (white) or

-	Aluminium painted to the same RAL colour as the frame profile Subsequent adjustment of blades not possible.

- 	end pieces on both sides

- 	With standard frame profile (-) or with special frame profile (-P)

-	with spring connection (-FM)

Product: SCHAKO type DSC 401 or 402

-	DSX: 1, 2, 3 or 4 slots

- 	Frame profile made of aluminium natural colour anodised (E6/EV1) or aluminium painted to RAL 9010 (white)

- 	Blades made of plastic, similar to RAL colour 9005 (black) or RAL 9010 (white)

- 	end pieces on both sides

- 	with narrow frame profile (-P) or wide frame profile (-PB)

-	with prong fastening (-BK)

Product: SCHAKO type DSX-...

-	DSX-XXL-W: 1 or 2 slots

-	Frame profile made of aluminium natural colour anodised (E6/EV1) or aluminium painted to RAL 9010 (white)

-	Blades made of plastic, similar to RAL colour 9005 (black) or RAL 9010 (white)

-	end pieces on both sides

-	with narrow frame profile (-P) or wide frame profile (-PB)

-	with prong fastening (-BK)

Product: SCHAKO type DSX-XXL-W-...

Accessories:

-	Cover (ÖA) to prevent soiling or damage during assembly, made of galvanised sheet steel with fixing via springs.

-	Throttle damper (-DK), manually adjustable from room side. Throttle made of stainless steel, with cable adjustment.

-	Rubber lip seal (-GD), made of special rubber (only AUDIXÒ-AW-R-...)

-	Box neck extension (-KHV) for wall thicknesses > 100 mm