Telephony silencer box AUDIX®

SPECIFICATION TEXT

Cross-talk sound attenuator box for supply air, with round connection spigot, with integrated silencer for installation in lightweight walls to connect one diffuser.

Airtight plenum box, with structure-borne noise insulation and integrated silencer to prevent cross-talk sound and for sound dampening in the duct. With abrasion-resistant absorption material attached on both sides inside. Fastening system for installation into the posts of lightweight walls.

Product: SCHAKO type AUDIX®-...-Z0

-	Cross-talk sound attenuator box for return air, with round connection spigot, with integrated silencer for installation in lightweight walls to connect one diffuser.

Product: SCHAKO type AUDIX®-...-A0

-	Cross-talk sound attenuator box for supply and return air, with one round connection spigot each for supply and return air, with integrated silencer for installation in lightweight walls to connect one diffuser.

Product: SCHAKO type AUDIX®-...-ZA

Building material class:

-	building material class A2 (non-flammable to DIN 4102-1) and A2-s1, d0 			          (non-flammable to EN 13501-1)

-	building material class B1 (slightly flammable to DIN 4102-1) and B/C 			           (slightly flammable to EN 13501-1) (standard)

Air diffusers (must be ordered separately):

-	nozzle jet diffuser ADSA-D0 (-55), 1-row

-	nozzle jet diffuser ADSA-VD (-61), 1-row

-	slot diffuser ADSC (-62), 1-slot

-	slot diffuser ADSC (-63), 2-slot

-	slot diffuser ADSX (-64), 1-slot

-	slot diffuser ADSX (-65), 2-slot

-	slot diffuser ADSX (-66), 3-slot

-	slot diffuser ADSX (-67), 4-slot

-	slot diffuser ADSXW (-68), 1-slot

-	slot diffuser ADSXW (-69), 2-slot

Simple assembly and disassembly for maintenance purposes

Height:

-	height 250 mm (-250)

-	height 350 mm (-350, standard)

-	height in mm, freely selectable (height ≥ 250 mm to 350 mm, always with 3 digits)

Length:

-	length 408 mm (-0408) (for diffuser length 400 mm)

-	length 508 mm (-0508, standard) (for diffuser length 500 mm)

-	length 608 mm (-0608) (for diffuser length 600 mm)

-	length 808 mm (-0808) (for diffuser length 800 mm)

-	length 1008 mm (-1008) (for diffuser length 1000 mm)

-	length 1208 mm (-1208) (for diffuser length 1200 mm)

-	length in mm, freely selectable (-xxxx, always with 4 digits, length ≥ 408 mm up to max. 1208 mm, always with 4 digits) (for diffuser ≥ 400 mm up to max. 1200 mm)

Mounting:

-	with magnetic fastening (standard)

Material:

-	galvanised sheet steel (standard)

Accessories:

-	Damper (-DK0 / -DK1)

-	without damper (-DK0) (standard).

-	with damper, made of galvanised sheet steel, in the connection spigot, manually adjustable from room side via cable, for simple air volume regulation (-DK2).

-	Rubber lip seal (-GD0 / -GD1)

-	without rubber lip seal (-GD0)

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.

-	Box neck (-KVS / -xxx)

-	standard box neck (-KVS).

-	box neck extension in mm, freely selectable (-xxx, always with 3 digits), required for wall thickness > 100 mm up to max. 350 mm.

-	Fixing lug (-B0 / -BL)

-		without fixing lug (-B0)

-	with fixing lug (-BL), made of galvanised sheet steel.

-	Cover (-OA0 / -OA1)

-	without cover (-OA0)

-	with cover (-OA1) (SCHAKO recommendation), made of cardboard.

Specification text for air diffusers

Nozzle jet diffuser ADSA (-55 / -61)

Nozzle jet diffuser ADSA-…, for installation in lightweight walls, with magnetic fastening (-MB) made of sheet steel.

-	With fixed plastic nozzles made of plastic material (standard).

Product: SCHAKO type ADSA-D0-... (-55)

-	With individually manually adjustable nozzles made of plastic material.

Product: SCHAKO type ADSA-VD-... (-61)

Air throw:

-	supply air (-Z0)

Length:

-	length 400 mm (-0400) (for AUDIX length 408 mm)

-	length 500 mm (-0500) (for AUDIX length 508 mm)

-	length 600 mm (-0600) (for AUDIX length 608 mm)

-	length 800 mm (-0800) (for AUDIX length 808 mm)

-	length 1000 mm (-1000) (for AUDIX length 1008 mm)

-	length 1200 mm (-1200) (for AUDIX length 1208 mm)

-	length in mm, freely selectable (-xxxx, always with 4 digits) (length ≥ 400 mm up to max. 1200 mm)  (for AUDIX length ≥ 408 mm up to max. 1208 mm)

Height:

-	nozzles 1-row (-1) (standard)

Single / band design:

-	single design (-N) (length max. 1200 mm, standard)

Material and paint (faceplate):

-	made of sheet steel (-SB, standard):

-	painted to the colour RAL 9010 (white, standard) (-9010)

-	painted to the colour RAL 9006 (white aluminium) (-9006)

-	painted to the colour RAL 9005 (black) (-9005)

-	painted to a RAL colour of your choice, freely selectable (-xxxx, always with 4 digits)

Nozzle colour:

-	Nozzles made of plastic material:

-	similar to RAL 9005 (black) (-DS)

-	similar to RAL 9006 (white aluminium) (-DA)

-	similar to RAL 9010 (white, standard) (-DW)

Slot diffuser ADSC (-62 / -63)

Slot diffuser ADSC-…, for installation in lightweight walls,

with magnetic fastening (-MB) made of sheet steel.

-	1-slot model.

Product: SCHAKO type ADSC-1-... (-62)

-	2-slot model.

Product: SCHAKO type ADSC-2-... (-63)

Air throw:

-	supply air (-Z0)

-	return air (-A0)

-	supply air/return air combination (-ZA)

Frame profile:

-	STANDARD frame profile (-R0)

-	special frame profile (-P0)

Frame surface:

-	Natural colour anodised aluminium (-ELOX, standard).

-	Aluminium painted to:

-	RAL colour 9006 (white aluminium) (-9006).

-	RAL colour 9010 (white) (-9010).

-	painted to a different RAL colour (freely selectable, at an extra charge) (-xxxx, always with 4 digits).

Blade colour:

-	Plastic (hard PVC):

-	Colour similar to RAL 9005 (black, standard) (-L9005).

-	Colour similar to RAL 9006 (white aluminium) (-L9006).

-	Colour similar to RAL 9010 (white) (-L9010).

-	painted to a freely selectable RAL colour (-Lxxxx, always with 4 digits)

-	without blade (-00000), only for return air, with perforated plate made of sheet steel painted to the colour of the blade, as screen.

Blade position for air jet:

-	without blades(-0), for return air, with perforated plate.

-	blades with vertical throw (-V) (standard)

Single / band design:

-	single design (-N) (length max. 1200 mm, standard)

Length:

-	length 400 mm (-0400) (for AUDIX length 408 mm)

-	length 500 mm (-0500) (for AUDIX length 508 mm)

-	length 600 mm (-0600) (for AUDIX length 608 mm)

-	length 800 mm (-0800) (for AUDIX length 808 mm)

-	length 1000 mm (-1000) (for AUDIX length 1008 mm)

-	length 1200 mm (-1200) (for AUDIX length 1208 mm)

-	length in mm, freely selectable (-xxxx, always with 4 digits) (length ≥ 400 mm up to max. 1200 mm) (for AUDIX length ≥ 408 mm up to max. 1208 mm)

Slot diffuser ADSX (-64 / -65 / -66 / -67)

Slot diffuser ADSX-…, for installation in lightweight walls,

with magnetic fastening (-MB) made of sheet steel.

-	1-slot model.

Product: SCHAKO type ADSX-1-... (-64)

-	2-slot model.

Product: SCHAKO type ADSX-2-... (-65)

-	3-slot model.

Product: SCHAKO type ADSX-3-... (-66)

-	4-slot model.

Product: SCHAKO type ADSX-4-... (-67)

Air throw:

-	supply air (-Z0)

-	return air (-A0)

-	supply air/return air combination (-ZA)

Frame profile:

-	STANDARD frame profile (10 mm) (-P0)

-	wide frame profile (16 mm) (-PB)

Frame surface:

-	Natural colour anodised aluminium (-ELOX, standard).

-	Aluminium painted to:

-	RAL 9006 (white aluminium) (-9006).

-	RAL 9010 (white) (-9010).

-	painted to a different RAL colour (freely selectable, at an extra charge) (-xxxx, always with 4 digits).

Blade colour:

-	Plastic (hard PVC):

-	Colour similar to RAL 9005 (black, standard) (-L9005).

-	Colour similar to RAL 9006 (white aluminium) (-L9006).

-	Colour similar to RAL 9010 (white) (-L9010).

Blade position for air jet:

-	blades with vertical throw (-V) (standard)

Single / band design:

-	single design (-N) (length max. 1200 mm, standard)

Length:

-	length 400 mm (-0400) (for AUDIX length 408 mm)

-	length 500 mm (-0500) (for AUDIX length 508 mm)

-	length 600 mm (-0600) (for AUDIX length 608 mm)

-	length 800 mm (-0800) (for AUDIX length 808 mm)

-	length 1000 mm (-1000) (for AUDIX length 1008 mm)

-	length 1200 mm (-1200) (for AUDIX length 1208 mm)

-	length in mm, freely selectable (-xxxx, always with 4 digits) (length ≥ 400 mm up to max. 1200 mm) (for AUDIX length ≥ 408 mm up to max. 1208 mm)

Slot diffuser ADSXW (-68 / -69)

Slot diffuser ADSXW-…, for installation in lightweight walls,

with magnetic fastening (-MB) made of sheet steel.

-	1-slot model.

Product: SCHAKO type ADSXW-1-... (-64)

-	2-slot model.

Product: SCHAKO type ADSXW-2-... (-65)

Air throw:

-	supply air (-Z0)

-	return air (-A0)

-	supply air/return air combination (-ZA)

Frame profile:

-	STANDARD frame profile (10 mm) (-P0)

-	wide frame profile (16 mm) (-PB)

Frame surface:

-	Natural colour anodised aluminium (-ELOX, standard).

-	Aluminium painted to:

-	RAL 9006 (white aluminium) (-9006).

-	RAL 9010 (white) (-9010).

-	painted to a different RAL colour (freely selectable, at an extra charge) (-xxxx, always with 4 digits).

Blade colour (hard PVC):

-	plastic:

-	Colour similar to RAL 9005 (black, standard) (-L9005).

-	Colour similar to RAL 9006 (white aluminium) (-L9006).

-	Colour similar to RAL 9010 (white) (-L9010).

Blade position for air jet:

-	blades with vertical throw (-V) (standard)

Single / band design:

-	single design (-N) (length max. 1200 mm, standard)

Length:

-	length 400 mm (-0400) (for AUDIX length 408 mm)

-	length 500 mm (-0500) (for AUDIX length 508 mm)

-	length 600 mm (-0600) (for AUDIX length 608 mm)

-	length 800 mm (-0800) (for AUDIX length 808 mm)

-	length 1000 mm (-1000) (for AUDIX length 1008 mm)

-	length 1200 mm (-1200) (for AUDIX length 1208 mm)

-	length in mm, freely selectable (-xxxx, always with 4 digits) (length ≥ 400 mm up to max. 1200 mm) (for AUDIX length ≥ 408 mm up to max. 1208 mm)