Overflow Box Model AUDIXG

Specification texts

Overflow box with ventilation openings of equal height, with integrated sound absorber to be built into lightweight walls as overflow unit for effectively preventing cross-talk transmission through the wall.

The AUDIXG have two housing shells with separation of structure-borne noise. Broad-band, volumetric insulation material free of mineral fibres and special insulating panels that prevent a buzzing sound allow their use in partition walls.

Box consisting of galvanised sheet steel as airtight overflow box. Integrated silencer comprising abrasion-resistant absorption material of building material class B1 (slightly flammable according to DIN 4102) attached on both sides, including a fitting system to assemble it into the columns of lightweight walls. Includes 2 cover frames with clamp mounting. Length 500 mm or 1000 mm.

Product: SCHAKO type AUDIXG-LG-...-BBOO-...

-	Overflow box with offset ventilation openings and 2 cover frames on both sides

Product: SCHAKO type AUDIXG-LV-...

-		Integrated silencer comprising an abrasion-resistant absorption material of building material class A2 (non-flammable to DIN 4102) attached on both sides.

Product: SCHAKO type AUDIXG-...-A2-...

-	with cover frame on one side / cover grille on one side

Cover grille with:		- FQ = 43% AUDIXG-...-AB43-...

- FQ = 46% AUDIXG-...-AB46-...

- FQ = 70% AUDIXG-...-AB70-...

-	with cover grille on both sides

Cover grille with:		- FQ = 43% AUDIXG-...-AA43-...

- FQ = 46% AUDIXG-...-AA46-...

- FQ = 70% AUDIXG-...-AA70-...

Accessories

-	Cover (-OA1) to prevent contamination or damage during assembly, made of galvanised sheet steel with

spring fastening.

-	Box neck extension (-KVS) for wall thicknesses >100 mm (-LV) or >125 mm (-LG) up to max. 350 mm

-	Mounting bracket (pair) made of galvanised sheet steel (-BW)