Fire Protection Unit Model BAK-240

Specification texts

Fire protection unit of resistance class K30-U, according to general building supervisory approval Z-41.3-574, suitable for installation in fire-resistant suspended ceilings designed as panelled ceilings in screw-type and spatulated design that meet the requirements of an independent component of being fire-resistant for 30 minutes in the event of a fire from top or bottom.

With metal-cased shut-off damper and visible screw mounting of the air diffuser. The shut-off damper is trigge-red by an inside and outside thermal trigger device, trigger temperature 72°C.

Product: SCHAKO type BAK-240

- 	With supply air - swirl diffuser, painted plastic or aluminium blades

- BDQJ-Q-SR-Z-…

- BDQJ-Q-SQ-Z-…

- 	With return air - swirl diffuser

- 	BDQJ-Q-SR-A-…

- BDQJ-Q-SQ-A-…

- 	With supply air - ceiling diffuser, painted sheet steel blades

- DQDL-Z-…

- 4DF-Z-…

- 	With return air - ceiling diffuser

- DQDL-A-…

- 4DF-A-…

-	 With supply air - ceiling diffuser,painted aluminium blades

- 4DE-Z-…

- 	With return air - ceiling diffuser

- 4DE-A-…

Accessories (at an extra charge):

- 	Electric limit switch for position indication "OPEN", swit-ching element containing one NC and one NO

contact

- Type ES-1A (-ESA)

Specification texts diffusers

(for supply air and return air)

Ceiling swirl diffuser BDQJ (-44)

Ceiling swirl diffuser BDQJ-..., particularly suitable for instal-lation in comfort rooms with high air change rates and for VAV installations with variable volumetric flows (between 40-100%). Cooling and heating modes are possible.

With square faceplate, with radial blade pattern. For supply air, with central pivoting, aerodynamic radially arranged con-tinuous air deflection blades in support blade profile sections made of plastic in a colour similar to RAL 9005 (-L9005, black, standard), similar to RAL 9006 (-L9006, grey), similar to RAL 9010 (-L9010, white) or made of aluminium painted to a RAL colour which can be freely selected (-Axxxx, subse-quent adjustment of blades not possible). Each plastic blade is adjustable from the diffuser faceplate without using any special device or dismounting the diffuser. Free cross-section, resistance and sound power level remain constant in all blade positions.

Product: SCHAKO type BDQJ-Q-SR-Z-...-PS-...

- 	With square faceplate, square blade pattern. For supply air, with central pivoting, aerodynamic radially arranged continuous air deflection blades in support blade profile sections made of plastic in a colour similar to RAL 9005 (-L9005, black, standard), similar to RAL 9006 (-L9006, grey), similar to RAL 9010 (-L9010, white) or made of aluminium painted to a RAL colour which can be freely selected (-Axxxx, subsequent adjustment of blades not possible).

Product: SCHAKO type BDQJ-Q-SQ-Z-...-PS-...

-	With square faceplate, circular blade pattern. For return air, without air deflection blades.

Product: SCHAKO type BDQJ-Q-SR-A-...-P0-...

- 	With square faceplate, square blade pattern. For return air, without air deflection blades.

Product: SCHAKO type BDQJ-Q-SQ-A-...-P0-...

Nominal sizes: NW 400 to 625

Drill pattern:

- Not reduced (-000, standard)

- Reduced drill pattern:

- Drill pattern 310 (-310, NW >310)

- Drill pattern 400 (-400, NW >400)

- Drill pattern 500 (-500, NW >500)