Floor convector CNV

Specification texts

Floor convectors CNV for heating in free convection, suitable for installation in floors and false floors, in particular in build-ings with large glass facades of large surface area reaching down to the floor. For shielding cold-radiating areas and for compensating high heat loads. The floor duct consists of gal-vanised sheet steel painted black to RAL 9005 with a frame made extruded aluminium profiles with legs adjustable from the room side and decoupled with rubber buffers. The ad-justable legs are additionally equipped with decoupled fas-tening lugs towards the room side. The heat exchanger con-sists of performance-optimised aluminium blades and copper pipes, including a ventilation valve. Towards the rooms the floor convector is equipped with a tread-resistant aluminium grille as linear grille or roll-down grille (optional).

Product: SCHAKO type CNV / CNVZ

Design variants

Width (W)

190 mm	-190

270 mm	-270

350 mm	-350

400 mm	-400

Height (H)

90 mm	-090

106 mm	-106

150 mm	-150

190 mm	-190

Nominal length (NL)

850 mm	-0850

1150 mm	-1150

1450 mm	-1450

1750 mm	-1750

2050 mm	-2050

2350 mm	-2350

2650 mm	-2650

2950 mm	-2950

3250 mm	-3250

3550 mm	-3550

3850 mm	-3850

Total length (LG)

Total length xxxx mm	-xxxx

Housing position

Standard model NL = LG	-S

Heat exchanger / Register centre, LG > NL	-M

Heat exchanger / Register left, LG > NL	-L

Heat exchanger / Register right, LG > NL	-R

Grille layer / Frame

Aluminium natural colour anodised E6/EV1	-G1

Aluminium black anodised E6/EV6	-G2

Aluminium bronze anodised E6/C33	-G3

Tread-resistant grille insert

Without grille	-00

Linear grille aluminium natural colour anodised E6/EV1	-L1

Linear grille aluminium black anodised E6/EV6	-L2

Linear grille aluminium bronze anodised E6/C33 -L3

Roll-down grille aluminium natural colour anodised E6/EV1 -R1

Roll-down grille aluminium black anodised E6/EV6 -R2

Roll-down grille aluminium bronze anodised E6/C33 -R3

Spigot diameter / Rubber lip seal

Without primary air connection spigot	-P0

Rectangular spigot, without rubber lip seal, H=106 mm	-P1

Spigot DN 78, without rubber lip seal, H=150 or H=190 mm	-P2

Spigot DN 98, without rubber lip seal, H=190 mm only	-P3

Spigot DN 123, without rubber lip seal, H=190 mm only	-P4

Spigot DN 78, with rubber lip seal, H=150 and H=190 mm only	-P5

Spigot DN 98, with rubber lip seal, H=190 mm only	-P6

Spigot DN 123, with rubber lip seal, H=190 mm only	-P7

Primary air connection spigot / Position

Without primary air connection spigot	-0

With primary air connection spigot, left end face	-1

With primary air connection spigot, right end face	-2

With primary air connection spigot, room side left	-3

With primary air connection spigot, room side right	-4

Connection position

Left end face	-W1

Right end face	-W2

Left end face - Room side	-W3

Right end face - Room side	-W4

Water connection

Register connection ½” male thread -0

Spigot nut female thread ¾“ Eurocone  -1

2-pipe valve set supplied loose -2

With water connection, flexible ½” male thread -3

With straight-through valve **, shut-off valve and actuator thermal 24 V 2P, LGmin = NL+100 mm -4

With straight-through valve **, shut-off valve and actuator thermal continuous 24 V, LGmin = NL+100 mm -5

With straight-through valve **, shut-off valve and actuator continuous 24 V (motorised), LGmin=NL+100 mm -6

Electrical junction box

Without electrical junction box	-S0

Electric junction box, with terminal strip, internally prewired -	-S1

End piece

Band design, centre part without end piece 	-E0

Band design with right end piece	-ER

Band design with left end piece	-EL

Single convector with 2 end pieces	-E2

External coating

Housing painted internally and externally to - RAL 9005 -	-A1

Housing painted externally - special paint - as rust protection with polyester powder (on request)	-A2

With impact sound insulation 3 mm, bonded over the entire surface	-A3

Adjusting legs

Adjusting legs 70 mm	-07

Adjusting legs 130 mm	-13

Protective mounting cover

Without protective mounting cover	-M0

With cardboard insert, not tread-resistant 	-M1

With tread-resistant wooden insert	-M2

CNVZ (Accessories) - Dummy element without interior parts for CNV

Width (W)

190 mm	-190

270 mm	-270

350 mm	-350

400 mm	-400

Height (H)

90 mm	-090

106 mm	-106

150 mm	-150

190 mm	-190

Angle α (°)

Straight dummy plate (α=180°)	-180

Corner piece 035≤xxx≤325 (α from 35° to 325°)	-xxx

Length L (mm)

Dummy plate 0600≤xxxx≤3000	-xxxx

Corner piece (L=xxxx according to Table 5)	-xxxx

Grille layer / Frame

Aluminium natural colour anodised E6/EV1	-G1

Aluminium black anodised E6/EV6	-G2

Aluminium bronze anodised E6/C33	-G3

Tread-resistant grille insert

Without grille	-00

Linear grille aluminium natural colour anodised E6/EV1	-L1

Linear grille aluminium black anodised E6/EV6	-L2

Linear grille aluminium bronze anodised E6/C33	-L3

Roll-down grille aluminium natural colour anodised E6/EV1	-R1

Roll-down grille aluminium black anodised E6/EV6	-R2

Roll-down grille aluminium bronze anodised E6/C33	-R3

Spigot diameter / Rubber lip seal

Without primary air connection spigot	-P0

Rectangular spigot, without rubber lip seal, H=106 mm	-P1

Spigot DN 78, without rubber lip seal, H=150 or H=190 mm	-P2

Spigot DN 98, without rubber lip seal, H=190 mm only	-P3

Spigot DN 123, without rubber lip seal, H=190 mm only	-P4

Spigot DN 78, with rubber lip seal, H=150 and H=190 mm on-ly	-P5

Spigot DN 98, with rubber lip seal, H=190 mm only	-P6

Spigot DN 123, with rubber lip seal, H=190 mm only	-P7

Primary air connection spigot / Position

Without primary air connection spigot	-0

With primary air connection spigot, left end face	-1

With primary air connection spigot, right end face	-2

With primary air connection spigot, room side left	-3

With primary air connection spigot, room side right	-4

End piece

Band design, centre part without end piece 	-E0

Band design with right end piece	-ER

Band design with left end piece	-EL

Single convector with 2 end pieces	-E2

External coating

Housing painted internally and externally to - RAL9005 -	-A1

Housing painted externally - special paint - as rust protection with polyester powder (on request)	-A2

With impact sound insulation 3 mm, bonded over the entire surface	-A3

Adjusting legs

Adjusting legs 70 mm	-07

Adjusting legs 130 mm	-13

Protective mounting cover

Without protective mounting cover	-M0

With cardboard insert, not tread-resistant 	-M1

With tread-resistant wooden insert	-M2

Cuts / Bevel cuts

Without cuts in dummy element	-A0

With rectangular cuts in dummy element	-A1

With round cuts in dummy element	-A2

With bevel cut on dummy element	-A3

Soundproofing bulkhead

Without soundproofing bulkhead in dummy element -S0

Soundproofing bulkhead with centre covering, 2 bulkhead sheets made of galvanised sheet steel, coated in black and a centre covering made of 2-mm aluminium plate, natural colour anodised. Bulkhead sheets mounted in duct ex works, space in-between filled with insulating material to be provided on site	S1