Combination ceiling slot diffuser für supply ans return air COMBIDSC

Specification text

Combination slot diffuser for supply and return air suitable for wall or ceiling mounting. Highly inductive slot diffuser on the supply air side, free cross-section, resistance and sound power level constant in all blade positions.

Supply air element with pivoting air deflection blades. Return air element without blades, with perforated plate made of sheet steel painted to RAL 9005 (black).

Product: SCHAKO type COMBIDSC-...-ZA-…

Model (number of slots):

-	2-slot (1 for supply air / 1 for return air) (-2)

-	4-slot (2 for supply air / 2 for return air) (-4)

Frame made of extruded aluminium profile, consisting of:

-	Frame profile:

-	Standard frame profile (-R0)

-	Narrow frame profile (-S0)

-	Special frame profile (-P0)

-	Frame surface:

-	Natural colour anodised (standard, -ELOX)

-	Painted to RAL 9006 (white aluminium, -9006)

-	Painted to RAL 9010 (white, -9010)

-	Painted to a different RAL colour (-xxxx)

Blade colour:

Supply air element with pivoting air deflection blades in sup-port profile shape made of plastic material (hard PVC). Re-turn air element with painted perforated plate:

-	Blade colour similar to RAL 9005 (black) / perforated plate painted to RAL 9005 (black) (-L9005) (standard).

-	Blade colour similar to RAL 9006 (white aluminium) / perforat-ed plate painted to RAL 9006 (white aluminium) (-L9006).

-	Blade colour similar to RAL 9010 (white) / perforated plate painted to RAL 9010 (white) (-L9010).

-	Blade RAL colour can be freely selected / perforated plate in the same colour (-Lxxxx).

Blade position for air jet:

-	Blades with vertical throw (-V).

-	Blades with horizontal one-way throw (-S).

Length / Model:

Single design (-N)

-	1000 mm (length of box KL = 1040 mm) (-N-01000).

-	1500 mm (length of box KL = 1540 mm) (-N-01500).

-	Length in mm, can be freely selected (-N-xxxxx, always with 5 digits).

Band design (-B)

-	Length in mm, as band (-B-xxxxx).

Available lengths according to SCHAKO standard for band design. With connecting pins, supplied loose (2 for each connection)

Depending on use, the combination slot diffuser COMBIDSC is only available with plenum box or dummy piece.

Mounting:

-	Permanent connection (-FV, standard).

-	Only possible with plenum box.

-	Standard for the models COMBIDSC-R0 / COMBIDSC-S0 and COMBIDSC-P0.

-	The slot diffuser is permanently connected to the plenum box.

-	Concealed mounting (-VM)

-	Only possible with plenum box.

-	Possible for the models COMBIDSC-R0 / COMBIDSC-P0 and COMBIDSC-S0-Z2 (with additional profile).

-	Not possible for the models COMBIDSC-S0-Z0 / COMBIDSC-S0-Z1 / -Z3.

-	The slot diffuser is screwed to the pole brace in the plenum box housing with concealed screws.

-	Clamp strap (-KB, standard)

-	Only possible for the model with dummy piece (-BS1) and without plenum box.

-	Screws and clamp straps are supplied loose.

-	Possible for the models COMBIDSC-R0 / COMBIDSC-P0 and COMBIDSC-S0-Z2 (with additional profile).

-	Not possible for the models COMBIDSC-S0-Z0 / COMBIDSC-S0-Z1 / -Z3.

--	The slot diffuser is screwed to the clamp strap with con-cealed screws (included in delivery).

-	For mounting, access on the rear is not required!

-	Mounting with counter pole brace (-GT)

-	Only possible for the model with dummy piece (-BS1) and without plenum box.

-	Screws and clamp straps are supplied loose.

-	Possible for the models COMBIDSC-R0 / COMBIDSC-P0 and COMBIDSC-S0-Z2 (with additional profile).

-	Not possible for the models COMBIDSC-S0-Z0 / COMBIDSC-S0-Z1 / -Z3.

-	The slot diffuser is screwed to the counter pole brace (pole brace strap) with concealed screws (included in delivery).

-	For mounting, access on the rear is required!

Accessories:

-	End pieces made of aluminium (same colour as frame).

-	Supplied loose (-ES, pair) (standard).

-	Mounted ex works on both sides (-EB).

-	Mounted ex works on the left side (-EL).

-	Mounted ex works on the right side (-ER).

-	Without end piece (-E0).

-	Additional profile made of aluminium (same colour as frame), only possible for COMBIDSC-S0:

-	Z I (-Z1): connection of ceiling panels.

-	Z II (-Z2): connection of panelled ceilings.

-	Z III (-Z3): connection of ceiling panels.

-	Without additional profile (-Z0).

-	Dummy piece (only possible without plenum box), mounting only possible with (-KB, standard) or counter pole brace (-GT).

-	Made of sheet steel painted to RAL 9005 (black) (-BS1).

-	Without dummy piece (-BS0, only possible in connec-tion with plenum box).

-	Plenum box (-ASK-26), made of galvanised sheet steel (-SV), with fixing lugs, without riveting nut (-E0, stand-ard) or with riveting nut (-EM).

-	Model (number of slots):

-	2-slot (1 for supply air / 1 for return air) (-2)

-	4-slot (2 for supply air / 2 for return air) (-4)

-	Single / band design:

-	Single length (-N, length of plenum box max. 1500 mm)

-	Band design (-B, available lengths according to SCHAKO standard for band design)

-	Length:

-	1000 mm (-01000)

-	1500 mm (-01500)

-	Length in mm, can be freely selected (-xxxxx, al-ways with 5 digits)

-	Mounting of box:

-	Permanent connection (-FV) (standard).

-	Concealed mounting (-VM) (only possible for the models COMBIDSC-R0 and for COMBIDSC-P0 and COMBIDSC-S0-Z2).

-	Material:

-	Galvanised sheet steel (-SV) (standard).

-	Damper:

-	Without damper (-DK0) (standard).

-	With damper made of galvanised sheet steel, ad-justable, for simple air volume regulation:

-	In the plenum box housing (with lateral spigot position S1 and S2) (-DK1).

-	In the connection spigot, with cable-operated adjustment (with spigot position from above S0) (-DK2).

-	Rubber lip seal:

-	Without rubber lip seal (-GD0)

-	With rubber lip seal (-GD1) made of special rub-ber, at the connection spigot.

-	Insulation:

-	Without insulation (-I0)

-	With box insulation inside (-Ii), thermal insulation at the inside of the plenum box.

-	With box insulation outside (-Ia), thermal insula-tion at the outside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS)

-	Height of plenum box in mm, freely selectable (-xxx) (minimum height = spigot diameter + 47 mm, always with 3 digits)

-	Box neck:

-	Standard box neck (-KVS)

-	Box neck in mm, freely selectable (-xxx) (mini-mum height = 45 - 200 mm, always with 3 digits)

-	Spigot position:

-	Spigot from above (-S0).

-	Lateral spigots on both sides (-S1) (standard).

-	Lateral spigot on one side (-S2).

-	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	Spigot diameter in mm, freely selectable (-xxx, always with 3 digits).

-	Suspension:

-	Without riveting nut (-E0).

-	With riveting nut (-EM), made of brass.

-	Corner angles (-EW-26), frame and dummy profile made of extruded aluminium profile. With 4 fishplates (-VL, in-cluded in delivery) made of aluminium (same colour as frame), supplied loose.

-	Model (number of slots):

-	2-slot (1 for supply air / 1 for return air) (-2)

-	4-slot (2 for supply air / 2 for return air) (-4)

-	Frame profile:

-	Standard frame profile (-R0)

-	Narrow frame profile (-S0)

-	Special frame profile (-P0)

-	Frame surface:

-	Natural colour anodised aluminium (standard, -ELOX)

-	Aluminium painted to

-	RAL 9006 (white aluminium, -9006)

-	RAL 9010 (white, -9010)

-	Painted to a different RAL colour (-xxxx)

-	Dummy profile colour: made of painted aluminium

-	Similar to RAL 9005 (black) (-B9005) (standard).

-	Similar to RAL 9006 (white aluminium) (-B9005).

-	Similar to RAL 9010 (white) (-B9010).

-	RAL colour can be freely selected (Bxxxx).

-	Angle between sides:

-	90° (-090).

-	Angle as required (-xxx), values between  = 90°

(-090, standard) and 170° (-170) are possible.

-	Left-side length (a):

-	Standard length L=250 for 2-slot models / L=400 for 4-slot models

-	Right-side length (b):

-	Standard length L=250 for 2-slot models / L=400 for 4-slot models

-	Additional profile:

-	Without additional profile (-Z0) (standard).