Room Air-Conditioning Cultra-Studioline

Specification texts

Plug-in room air-conditioning module for decentralised air-conditioning of rooms with high acoustic requirements, such as offices, medical practices, meeting rooms, sound and television studios for cooling and/or heating.

For installation in walls and ceilings or for in-front-of-the-wall installation.

The fan unit consists of double-sided, intake-operated, dynamically balanced, centrifugal blowers with forward directed blades and direct actuator.

The fan units are equipped with a highly efficient, electronically commutated EC motor with maintenance-free ball bearing for a long service life. The EC fan can be activated by 2-10 V and is almost infinitely variable. The housing and the fan wheel are made of plastic and are optimised for the lowest possible sound pressure.

The heat exchangers consist of a galvanised sheet steel frame with copper pipes and aluminium blades in 
2-pipe and 4-pipe design.

Condensate pan in compliance with VDI 6022, made of stainless steel sheet, suitable for horizontal and vertical installation.

Filter efficiency ISO Coarse 30% (ISO 16890), regenerative synthetic fibre mat on a plastic frame.

Easy maintenance and filter exchange. The inspection plate is quick and easy to open by means of a removable lock.

The devices comply with the EMC requirement class C1 according to EN 61800.

Product:	SCHAKO

Family: 		Room air-conditioning module Cultra Studioline

### Cultra Studioline models

Type

Room air-conditioning module Cultra Studioline	-CSL

Size

Size 1		-1

Size 2		-2

Size 3		-3

System (water register version)

2-pipe register 1 row of pipes (heating)		-R1

2-pipe register 3 rows of pipes (cooling or heating)		-R3

4-pipe register 1 and 3 rows of pipes (cooling and heating)	-L4

Total height

Total height 2500 mm	-2500

Total height xxxx mm	-xxxx

Housing colour

Housing unpainted	-0

Black housing, painted to RAL 9005	-1

White housing, painted to RAL 9010	-2

White housing, painted to RAL 9016	-3

Grey housing, painted to RAL 9006	-4

Mounting position

Mounting type vertical, sec. air grille and inspection in the room	-VR

Mounting type horizontal in the ceiling		-H0

Adjusting legs

without adjusting legs	-0

with adjusting legs	-1

Supply air diffuser

Supply air diffuser DBB-A	-D1

Colour of the supply air diffuser

Colour of supply air diffuser: RAL 9010 white, white blades	-22

Faceplate/frame colour x, blade/nozzle colour y		-xy

Secondary air grille

Secondary air grille PAZ		-R1

Colour of the secondary air grille

Colour of secondary air grille: RAL 9010 white		-22

Faceplate/frame colour x, blade/nozzle colour y		-xy

Sliding connection spigot for supply air diffuser and secondary air grille

Without sliding connection spigot (air diffusers in the device)	-M0

With sliding connection spigot, adjusting range: 25 to 105 mm	-M1

With sliding connection spigot, adjusting range: 75 to 205 mm	-M2

Primary air connection spigot position

Without primary air connection spigot		-P0

Primary air connection spigot on the left side of the box	-P1

Primary air connection spigot on the right side of the box	-P2

Primary air connection spigot on the top centre of the box	-P7

Primary air connection spigot in the centre rear of the box	-P9

Primary air spigot diameter

Without primary air connection spigot	-0

Spigot diameter DN78	-1

Spigot diameter DN98	-2

Spigot diameter DN123	-3

Water connection position

Water connection top left	-W1

Water connection top right	-W2

Water connection bottom left	-W3

Water connection bottom right	-W4

Water connection centre left side	-W5

Water connection centre right side	-W6

Water connection bottom left side	-W7

Water connection bottom right side	-W8

Mounting of hydraulic regulation

On-site mounting (pieces are supplied loose for on-site mounting

outside the room air-conditioning module)		-000

cooling valve x, heating valve y, actuators z are mounted ex works	-xyz

Electric connection position

Electric connection top left	-S1

Electric connection top right	-S2

Electric connection bottom left	-S3

Electric connection bottom right	-S4

Electric connection centre left side	-S5

Electric connection centre right side	-S6

Electric connection bottom left side	-S7

Electric connection bottom right side	-S8

Additional control and regulation elements

Without additional control and regulation elements		-0

With fault message output		-1

Condensate connection position

Condensate connection top left	-K1

Condensate connection top right	-K2

Condensate connection bottom left	-K3

Condensate connection bottom right	-K4

Condensate connection centre left side	-K5

Condensate connection centre right side	-K6

Condensate connection bottom left side	-K7

Condensate connection bottom right side	-K8

Condensate pump

Without condensate pump	-0

With condensate pump Si-10, mounted ex works	-1

### Accessories

Hydraulic connections

EDE-13 500 mm	-1

EDE-13 800 mm	-2

EDE-13 1200 mm	-3

AG male thread ½”	-A

AG male thread ¾”	-B

ÜMF flat seal spigot nut ½”	-C

ÜMF flat seal spigot nut ¾”	-D

R-AG-D rotating male thread ½”	-E

R-AG-D rotating male thread ¾”	-F

C-RV bend plug-in fitting DN15	-H

CE-RV bend plug-in fitting with ventilation DN15	-J

RV straight connector / plug-in fitting DN15	-L

Room thermostat

RDG160T	-TR05

RDG160KN	-TK02

Rotary drive for 6-way ball valve

GDB341.9E	-AR01

GDB161.9E	-AR02

GDB111.9E	-AR03

6-way ball valve

VWG41.10-0.25-0.40		-V601

VWG41.10-0.25-0.65		-V602

VWG41.10-0.25-1.00		-V603

VWG41.10-0.40-0.65		-V604

VWG41.10-0.40-1.00		-V605

VWG41.10-0.40-1.30		-V606

VWG41.10-0.40-1.60		-V607

VWG41.10-0.65-1.00		-V608

VWG41.10-0.65-1.30		-V609

VWG41.10-0.65-1.60		-V610

VWG41.10-1.00-1.30	-V611

VWG41.10-1.00-1.60	-V612

VWG41.10-1.00-1.90	-V613

VWG41.10-1.30-1.60	-V614

VWG41.10-1.30-1.90	-V615

VWG41.10-1.60-1.90	-V616

VWG41.10-1.90-1.90	-V617

VWG41.10-0.25-1.30	-V618

VWG41.10-0.25-1.60	-V619

VWG41.10-0.25-1.90	-V620

VWG41.10-0.40-0.40	-V621

VWG41.10-0.40-1.90	-V622

VWG41.10-0.65-0.65	-V623

VWG41.10-0.65-1.90	-V624

VWG41.10-1.00-1.00	-V625

VWG41.10-1.30-1.30	-V626

VWG41.10-1.60-1.60	-V627

VWG41.20-0.65-2.50	-V628

VWG41.20-1.00-2.50	-V629

VWG41.20-1.60-2.50	-V630

VWG41.20-1.60-3.45	-V631

VWG41.20-2.50-3.45	-V632

VWG41.20-2.50-4.25	-V633

VWG41.20-4.25-4.25	-V634

VWG41.20-0.25-2.50	-V635

VWG41.20-0.25-3.45	-V636

VWG41.20-0.25-4.25	-V637

VWG41.20-0.40-2.50	-V638

VWG41.20-0.40-3.45	-V639

VWG41.20-0.40-4.25	-V640

VWG41.20-0.65-3.45	-V641

VWG41.20-0.65-4.25	-V642

VWG41.20-1.00-3.45	-V643

VWG41.20-1.00-4.25	-V644

VWG41.20-1.30-2.50	-V645

VWG41.20-1.30-3.45	-V646

VWG41.20-1.30-4.25	-V647

VWG41.20-1.60-4.25	-V648

VWG41.20-2.50-2.50	-V649

VWG41.20-3.45-3.45	-V650