Ceiling Displacement Diffuser DAV

Specification texts

Square ceiling displacement diffuser for use in supply and return air installations of sales rooms, production halls,

kitchens, etc. up to 4 m in height. For low-induction introduction of supply air from the ceiling, for installation flush with the

ceiling or freely suspended. It produces a bell-shaped displacement flow, in order to form fresh air zones in rooms

contaminated with hazardous substances or odours.

Consisting of a square faceplate easy to clean, with star-shaped perforation, made of perforated sheet steel painted to

RAL 9010 (white). The supply air model is additionally provided with a baffle plate and a sheet steel air guide funnel

painted to RAL 9005 (black). It is fastened by concealed mounting (-VM) using a central fastening screw.

Product: SCHAKO type DAV-Q-Z-...

-		Return air version without baffle plate and without air guide funnel

Product: SCHAKO type DAV-Q-A-...

-		with screw mounting (-SM), only for model with ball-impact guard (-BS)

-		Screw mounting with concealed mounting (-VS), only for model with ball-impact guard (-BS) (only for NW 800)

Round ceiling displacement diffuser for use in supply and return air installations of sales rooms, production halls,

kitchens, etc. up to 4 m in height. For installation flush with the ceiling or freely suspended. For low-induction introduction

of supply air from the ceiling, for installation flush with the ceiling or freely suspended. It produces a bell-shaped

displacement flow, in order to form fresh air zones in rooms contaminated with hazardous substances or odours.

Consisting of a round faceplate easy to clean, with star-shaped perforation, made of perforated sheet steel painted to

RAL 9010 (white). The supply air model is additionally provided with a baffle plate and a sheet steel air guide funnel

painted to RAL 9005 (black). It is fastened by concealed mounting (-VM) using a central fastening screw.

Product: SCHAKO type DAV-R-Z-...

-		Return air version without baffle plate and without air guide funnel

Product: SCHAKO type DAV-R-A-...

Accessories:

-		with plenum box (SK-R-05-Z-...) made of galvanised sheet steel, with integrated perforated straightener, lateral connection spigot and fixing lugs.

-		includes a damper adjustable at the front side in the plenum box for air volume regulation (-DK1)

-		with cable-operated adjustment (-DK2)

-		Volumetric flow meter (-VME1) in connection spigot

-		With rubber lip seal (-GD1) at the connection spigot

-		with thermal insulation

-		internal (-Ii)

-		external (-Ia)

-		Height of plenum box can be freely selected, xxx in mm, minimum height = spigot diameter + 137 mm, but at least 235 mm

-		Spigot diameter can be freely selected, xxx in mm

-		Spigot position:

-		S0 = spigot from above

-		S1 = 1 lateral spigot on the box (standard)

-		S2 = 2 spigots offset by 90°

-		S3 = 2 spigots offset by 180°

-		S5 = 2 spigots arranged next to each other

-		with plenum box (SK-R-05-A-...) made of galvanised sheet steel, with lateral connection spigot and fixing lugs		-		includes a damper adjustable at the front side in the plenum box for air volume regulation (-DK1)

-		with cable-operated adjustment (-DK2)

-			Volumetric flow meter (-VME1) in connection spigot

-			With rubber lip seal (-GD1) at the connection spigot

-			with thermal insulation

-		internal (-Ii)

-		external (-Ia)

-			Height of plenum box can be freely selected, xxx in mm, minimum height = spigot diameter + 137 mm, but at least 235 mm (For SK-R-05-Z-...-DK1/-DK2-...-S0, observe special height of plenum box (see p. 6)

-			Spigot diameter can be freely selected, xxx in mm

-			Spigot position:

-		S0 = spigot from above

-		S1 = 1 lateral spigot on the box (standard)

-		S2 = 2 spigots offset by 90°

-		S3 = 2 spigots offset by 180°

-		S5 = 2 spigots arranged next to each other

-	Ball-impact guard (-BS), made of steel with high-quality powder coating in RAL 9010 (white), other RAL colours possible at an extra charge (possible only for DAV-Q-... with screw mounting and for NW 800 only with concealed mounting).