Ceiling Diffuser Model DBB

Specification texts

Ceiling air diffuser type DBB for supply and return air, in rectangular design, free cross-section, resistance and noise level remain constant in all blade positions. Consisting of faceplate with individually adjustable pivoting air deflection blades.

Product: SCHAKO type DBB-…

Model:

-	longitudinal slots only (-A).

-	longitudinal slots and transverse slots on one side (-B). (available from length 425 mm / height 215 mm)

-	longitudinal slots and transverse slots on both sides (-C). (available from length 425 mm / height 215 mm)

Air throw:

-	supply air 1-way (for DBB-A) (-Z1)

-	supply air 2-way (for DBB-A and DBB-B) (-Z2)

-	supply air 3-way (for DBB-B and DBB-C) (-Z3)

-	supply air 4-way (for DBB-C) (-Z4)

-	return air, without blades (-AA)

-	return air with blades (-AB)

Length:

-	325 mm (-00325)

-	425 mm (-00425)

-	525 mm (-00525)

-	625 mm (-00625)

-	825 mm (-00825)

-	1025 mm (-01025)

-	1225 mm (-01225)

-	length in mm, freely selectable, for band design (for length BL > 1225 mm: 2-part for a length of band

BL ≤ 2437 mm, multi-part for a length of band > 2437 mm) (always with 5 digits).

Height:

-	115 mm (-115)

-	215 mm (-215)

-	315 mm (-315)

Single / band design:

-	single design (-N) (standard)

-	Band design (-B) (available lengths according to SCHAKO standard for band design) (for length BL > 1225 mm, mod-ule length max. 1225 mm, only possible for model DBB-A).

Material / paint (faceplate):

-	Sheet steel (-SB):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to another RAL colour, freely selectable (-xxxx)

-	Galvanised sheet steel (-SV-0000) (only possible without paint).

-	Natural colour anodised aluminium (E6/EV1, only possible with concealed mounting, only possible with

ELOX paint) (-AL-ELOX)

Blade colour:

-	Without blades (-00000) (standard for return air).

-	Plastic:

-	similar to RAL colour 9005 (black) (-L9005).

-	similar to RAL colour 9010 (white, standard) (-L9010).

-	Aluminium:

-	painted to the RAL colour of the faceplate (at an extra charge). The painted blades cannot be

adjusted subsequently (-Axxxx) (always with 5 digits).

-	natural colour anodised (-AELOX).

Mounting:

-	Screw mounting (-SM, standard)

-	screws must be provided on site.

-	Concealed mounting (-VM, standard for faceplate made of aluminium).

-	only possible with plenum box (plenum box can also be provided on site).

-	the counter pole brace to be provided by customer when delivered without plenum box.

-	In concealed mounting, the ceiling air diffuser is fixed to the plenum box with a pole brace and

hexagonal socket head screws (DIN EN ISO 4762 M6).

Accessories:

-	Plenum box, in rectangular design, made of galvanised sheet steel (-SV, standard), housing with round connection spigot and mounting brackets.

-	Air diffuser:

-	for ceiling air diffuser DBB-…-A… (return air) (-48) (inside painted to RAL colour 9005 [black]).

-	for ceiling air diffuser DBB-…-Z… (supply air) (-50) (with integrated perforated straightener).

-	Length:

-	325 mm (-00325)

-	425 mm (-00425)

-	525 mm (-00525)

-	625 mm (-00625)

-	825 mm (-00825)

-	1025 mm (-01025)

-	1225 mm (-01225)

-	length in mm, freely selectable, for band design (for length BL > 1225 mm: 2-part for a length of band BL ≤ 2437 mm, multi-part for a length of band > 2437 mm) (always with 5 digits).

-	Height:

-	115 mm (-115)

-	215 mm (-215)

-	315 mm (-315)

-	Single / band design:

-	single design (-N) (standard).

-	band design (-B) (for length BL > 1225 mm, avail-able lengths according to SCHAKO standard

for band design).

-	Mounting:

-	Screw mounting (-SM) (standard, screws must be provided on site).

-	concealed mounting (-VM).

-	Damper:

-	without damper (-DK0) (standard).

-	with damper (-DK1), made of galvanised sheet steel, in the plenum box housing, adjustable, for simple air volume regulation. Standard with lateral spigot position (-S1).

-	with damper (-DK2), same as DK1, but with cable-operated adjustment, standard with spigot position from above (-S0) and front side spigot position (-S4).

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.

-	Insulation:

-	without insulation (-I0) (standard).

-	with internal insulation (-Ii), thermal insulation inside the plenum box.

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS).

-	height of plenum box in mm, freely selectable (-xxx) (minimum height [KHS] with spigot positions -S1 and -S4 = spigot diameter + 87 mm, but at least 200 mm) (always with 3 digits).

-	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	spigot diameter in mm, freely selectable (-xxx, always with 3 digits) (with spigot positions -S0 and -S4, if the spigot diameter is increased, only the offset plenum box shape is available).

-	Spigot position:

-	Spigot from above (-S0).

-	Lateral spigot on the plenum box (-S1) (standard).

-	Front side spigot (-S4, not possible for band de-sign).

-	Hit-and-miss damper (-SN / -SS)

-	without hit-and-miss damper (-SN) (standard).

-	with hit-and-miss damper (-SS)

-	for air volume regulation, made of galvanised sheet steel.

-	VM model is only possible with plenum box or on-site counter pole.

-	Ball-impact guard (-B0 / -BS)

-	without ball-impact guard (-B0) (standard).

-	with ball-impact guard (-BS)

-	not possible for DBB-…-AL-ELOX.

-	made of steel painted to the RAL colour of the faceplate.