Round duct blade diffuser DBBRR

Specification texts

Round duct blade diffuser suitable for connection to DIN ducts. With integrated, manually adjustable air deflection blades. Sound power level and pressure loss remain constant in all blade positions.

Product: SCHAKO type DBBRR-Z-...

-	for return air, without air deflection blades

Product: SCHAKO type DBBRR-A-...

-	Nominal width:

-	200 mm (-200)

-	224 mm (-224)

-	250 mm (-250)

-	280 mm (-280)

-	315 mm (-315)

-	355 mm (-355)

-	400 mm (-400)

-	450 mm (-450)

-	500 mm (-500)

-	560 mm (-560)

-	630 mm (-630)

-	Length:

-	1-part: 500 / 750 / 1000 (-0500/-0750/-1000)

-	2-part: 1500 / 1750 / 2000 (-1500/-1750/-2000)

-	Air throw pattern:

-	one-way horizontal throw (-E).

-	two-way horizontal throw (-B, standard).

-	vertical throw (-V).

-	crosswise throw (-K).

-	Return air without blades (-O).

-	Material and paint (round duct):

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel painted to RAL 9010 (white) (standard, -SB-9010).

-	Sheet steel painted to a freely selectable RAL colour (-SB-xxxx) (colour always with 4 digits).

-	Blade colour:

-	Without blades (-00000, only possible for return air).

-	With blades of plastic material:

-	Similar to RAL colour 9010 (-L9010, white).

-	Similar to RAL colour 9005 (-L9005, black) (standard).

-	With blades made of aluminium painted to the RAL colour of the round duct (-Axxxx) (colour always with 4 digits), painted blades cannot be subsequently adjusted.

-	Number of slots:

-	2-slot (-02).

-	4-slot (-04).

-	6-slot (possible from NW 280 upwards) (-06).

-	8-slot (possible from NW 355 upwards) (-08).

-	10-slot (possible from NW 500 upwards) (-10).

-	12-slot (possible from NW 500 upwards) (-12).

-	14-slot (possible from NW 500 upwards) (-14).

-	Mounting position:

-	3 o'clock (-3U).

-	6 o'clock (-6U, standard).

-	9 o'clock (-9U).

-	12 o'clock (-0U).

-	Hit-and-miss damper:

-	Without hit-and-miss damper (-SN).

-	With integrated hit-and-miss damper (-SS) for simple air volume and ductwork regulation, made of the same material as the round duct.

-	Fastening methods:

-	fastening hole

-	without fastening hole (-B0).

-	with fastening hole ø11.5 mm (-BB, standard).(Prepared for suspended installation by using an M8 threaded rod and an M8 nut to be provided on site).

Accessories (at an extra charge):

-	Rubber lip seal

-	Without rubber lip seal (-GD0).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

For more accessories, please refer to the separate documentation "Round duct system accessories".