Swirl Diffuser Model DHV

Specification texts

Ceiling swirl diffuser type DHV for connection to flexible ducts, consisting of faceplate, inlet and fixed nozzle-like swirl impellers.

Product: SCHAKO type DHV-...

Model:

-	with square faceplate and inlet nozzle, NW 100-400 (NW 100 made of sheet steel / NW 125-400 made of aluminium) (-Q)

-	with round faceplate and inlet nozzle NW 100-400

(NW 100 made of sheet steel / NW 125-400 made of aluminium) (-R)

-	with round faceplate and inlet nozzle NW 125-250 (made of plastic material) (-K)

Air throw:

-	supply air (-Z)

-	return air (-A)

Nominal size:

-	NW 100 (-100)

-	NW 125 (-125)

-	NW 160 (-160)

-	NW 200 (-200)

-	NW 250 (-250)

-	NW 315 (-315)

-	NW 400 (-400)

Material (faceplate):

-	made of sheet steel (-SB) (only for DHV-Q/R-... NW 100)

-	made of aluminium (-AL) (only for DHV-Q/R-... NW 125-400)

-	made of plastic material (-KU) (only for DHV-K-... NW 125-250)

Paint:

-	RAL colour 9010 (white) (standard) (-9010)

-	RAL colour can be freely selected (-xxxx, always with 4 digits) (not possible for DHV-K-...)

Mounting:

-	concealed mounting (-VM, standard)

-	Counter pole brace on site (without plenum box or transition piece)

-	with pole brace fixing (with plenum box or transition piece)

-	with screw mounting (-SM), standard for panelled cover and for connection to flexible ducts (without plenum box). (not possible for transition piece -US)

-	with clamp fastening (-KB), only for connection to flexible ducts (without plenum box)

-	Panelled cover plate (-PA000/-PA...)

-	without panelled cover plate (-P0000) (standard)

-	with panelled cover plate, made of sheet steel, painted to the selected colour 							(not possible for DHV-R)

-	NW 310 (-PA310), for DHV NW 100-200.

-	NW 400 (-PA400), for DHV NW 100-250.

-	NW 500 (-PA500), for DHV NW 100-315.

-	NW 600 (-PA600), for DHV NW 100-400.

-	NW 625 (-PA625), for DHV NW 100-400.

Accessories:

-	Transition piece (-U0/-US)

-	without transition piece (-U0) (standard)

-	with transition piece (-US) (natural aluminium, with internal counter pole brace for concealed mounting (VM), with integrated perforated straightener, for ceiling panels up to 20 mm thick (not possible for NW 400) (only possible with concealed mounting VM)

-	Plenum box (SK-R-09-...) with square design, for round air diffusers with round diffuser support, suitable for DHV-..., made of galvanised sheet steel (-SV), with fixing lugs.

-	Type of air:

-	supply air (-Z), with air diffuser plate.

-	return air (-A)

-	Nominal size:

-	NW 100 (-100)

-	NW 125 (-125)

-	NW 160 (-160)

-	NW 200 (-200)

-	NW 250 (-250)

-	NW 315 (-315)

-	NW 400 (-400)

-	Fastening:

-	Concealed mounting (-VM, standard)

-	Damper:

-	Without damper (-DK0) (standard)

-	with damper in plenum box/connection spigot, adjustable from below, for easy air volume regulation without dismounting the faceplate.

-	without cable-operated adjustment (-DK1)

-	with cable-operated adjustment (-DK2)

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard)

-	with rubber lip seal (-GD1), made of special rubber, at the connection spigot

-	Volumetric flow meter:

-	Without volumetric flow meter (-VME0) (standard)

-	with volumetric flow meter (-VME1) (not for use with a damper)

-	ROB version:

-	without ROB version (-ROB0) (standard)

-	Insulation:

-	without insulation (-I0) (standard)

-	with internal insulation (-Ii), thermal insulation inside the plenum box

-	with external insulation (-Ia), thermal insulation on the outside of the plenum box

-	Height of box:

-	Standard height of plenum box (-KHS)

-	height of box in mm, freely selectable (always with 3 digits)

(Min. height of plenum box [KHS] for NW 100-315 = spigot diameter øD + 137 mm, but at least

235 mm, for NW 400 = spigot diameter øD + 242 mm, but at least 340 mm) (With SK-R-09-Z-...-

DK1/-DK2-...-S0, observe special height of plenum box for NW 100)

-	Spigot diameter:

-	Standard spigot diameter (-SDS)

-	spigot diameter (D) in mm, freely selectable (-xxx, always three digits)

-	Spigot position:

-	Spigot from above (-S0)

-	1 lateral spigot on the plenum box (-S1) (standard)

-	2 lateral spigots, offset by 90° (-S2)

-	2 lateral spigots, offset by 180° (-S3)

-	2 spigots arranged next to each other (-S5)