Induction diffuser DISA-360

Specification text

Ceiling induction diffuser DISA-360 for installation in false ceilings Housing made of galvanised sheet steel. With foldable louvre grid type SCHAKO-PA or perforated sheet made of sheet steel painted to RAL 9010 (white, standard). Horizontal 2-pipe (standard) or 4-pipe register (optional) for cooling and heating, including galvanised sheet steel frame, copper pipes and aluminium blades Four-way supply air throw and air deflection blades (optional)

Width: 592-622 mm, height: 220 mm, length: 592-1247 mm

Product: SCHAKO type DISA-360

-	System

-	2-pipe system (-H), standard

-	4-pipe (-HT)

-	Without register (-BO)

-	Air deflection blades

-	Individually adjustable (-LE)

-	Blockwise adjustable (-LB)

-	Without air deflection blades (-OL)

-	Secondary air grille

-	Foldable perforated sheet, perforation Ø 6 mm (-SR, standard)

-	Foldable perforated sheet, perforation 8x8 mm (-SQ)

-	Foldable perforated sheet, perforation 12x5 (-RE)

-	Foldable perforated sheet, oval perforation 20x6 mm (-OB)

-	Louvre grid (-PA)

-	Foldable louvre grid PA

-	Nozzle configuration

-	B (standard)

-	C

-	D

-	E

-	Total width

-	592

-	597

-	617

-	622

-	Total length

-	for a total width of 592

- 592

- 1192

-	for a total width of 597

- 597

- 1197

-	for a total width of 617

- 617

- 1242

-	for a total width of 622

- 622

- 1247

-	Freely suspended installation

-	with freely suspended installation (-FM)

-	without freely suspended installation (-)

-	Water connection

-	left (-WS1)

-	right (-WS2)

-	Register paint

-	Unpainted register (-)

-	Register painted black (-R9005)

-	Arrangement of connecting pieces

-	horizontal with 1 connecting piece (-AS1)

-	horizontal with 2 connecting pieces (-AS2/AS3)

-	vertical with 1 connecting piece (-AS4)

-	vertical with 2 connecting pieces (-AS5/AS6)

-	Connecting piece diameter

-	Ø 98 mm

-	Ø 123 mm (standard)

Accessories

-	Rubber lip seal (-GD)

-	Flexible connection hoses

-	500 mm (-FA 500)

-	800 mm (-FA 800)

-	1200 mm (-FA 1200)

-	Volumetric flow measuring tube (-MR)

-	External thread flat sealing (-WA 1/2)

-	Condensation monitor

-	Control units

-	Valves

-	Actuators