Floor Induction Diffuser DISA-B

Specification text

Floor induction diffusers DISA-.B for installation in double or cavity floors Suitable for energy-efficient and comfortable air-conditioning of rooms with high comfort requirements. Consisting of a load-bearing housing made of galvanised sheet steel painted black on the inside with adjusting legs height-adjustable from the room side. Specific mounting plates on the adjusting legs allow levelling from the room side at a later stage at any time. For optimising the induction performance and minimising the sound power level, four nozzle versions made of non-flammable perforated nozzles and five nominal lengths are available.  The heat exchanger consists of copper pipes with pressed-on aluminium blades and a galvanised sheet steel frame. As standard, equipped with a register in 2-pipe design for heating or cooling mode and optionally 4-pipe design for heating and cooling mode. As standard, the registers are designed with ventilation openings. Grille layer design, linear grille SCHAKO-PA or optionally roll-down grille PA-R.

Width: 375 mm, Height: 181 mm, Length: 1000-2000 mm

Product: SCHAKO type DISA-B

-	System

-	4-pipe system (-HT), standard

-	2-pipe system (-H)

-	Without register (-BO)

-	Louvre grid

-	Louvre grid (-PA-3)

-	Roll-down grille (-PA-R)

-	Nozzle configuration

-	B (standard)

-	C

-	D

-	E

-	Nominal length (NL)

-	1000

-	1150

-	1300

-	1450

-	1600

-	1750

-	Total length (LG)

-	without integrated valve group: 2000 > LG ≥ NL

-	with integrated valve group: 2000 > LG ≥ NL + 150

-	Position of primary air plenum box

-	left (-L)

-	centred (-M)

-	right (-R)

-	Water connection

-	lateral left (-WS1)

-	lateral right (-WS2)

-	Front side left (-WS3)

-	Front side right (-WS4)

-	Register paint

-	Unpainted register (-)

-	Register painted black (-R9005)

-	Arrangement of connecting pieces

-	horizontal with 1 connecting piece (-AS1)

-	horizontal with 2 connecting pieces (-AS2/AS3)

-	Connecting piece diameter

-	Ø 98 mm

-	Ø 123 mm (standard)

-	Band design (-BA)

-	End piece on the left (-EL)

-	End piece on the right (-ER)

-	without end piece (-OE)

Accessories

-	Rubber lip seal (-GD)

-	Flexible connection hoses

-	500 mm (-FA 500)

-	800 mm (-FA 800)

-	1200 mm (-FA 1200)

-	Volumetric flow meter (-MR)

-	External thread flat sealing (-WA 1/2)

-	Mounting cover made of wood (-SW)

-	Condensation monitor

-	Valves

-	Actuators

-	Control units

-	Ball valves (-KH)

-	Valve group mounted on site.