Induction diffuser DISA-H

Specification text

Induction diffuser type DISA-H with horizontal throw, for installation preferably in hotels, hospitals and offices with suspended entrance hall or suspended ceiling panelling.

Consisting of a galvanised sheet steel housing with integrated non-flammable galvanised sheet steel nozzle plate available in three different configurations for small, medium and large air volumes.

As standard the devices are equipped with a heat exchanger with copper pipes and attached aluminium blades for the 2-pipe system for cooling or heating or the 4-pipe system for cooling and heating (optional).

The air-side connection of the induction units is made from behind using 1 or, optionally, 2 connecting pieces.

For easy mounting, the devices are equipped ex works with mounting bores on the top side.

Depth: 600 mm, Height: 200 mm, Length: 900 - 1500 mm (with 300 mm division)

Product: SCHAKO type DISA-H

-	System

-	2-pipe system (-H), standard

-	4-pipe (-HT)

-	Nozzle configuration

-	D

-	E

-	F

-	Length

-	900

-	1200

-	1500

-	Water connection

-	left back (-WS1)

-	right back (-WS2)

-	Registers

-	Unpainted register (-)

-	Painted register (-R9005)

-	Number of connection pipes

-	With 1 connection pipe (-AS1, standard)

-	With 2 connection pipes (-AS2/AS3)

-	Connection pipe diameter

-	Ø 98 mm

-	Ø 123 mm (standard)

-	Ø 148 mm

-	Housing

-	Unpainted housing (-)

-	Painted housing (-R9005)

Accessories:

-	Rubber lip seal (-GD)

-	Volumetric flow measuring tube (-MR)

-	Box neck extension for supply air -KZ (60...200)

-	Box neck extension for secondary air -KS (60...200)

-	Flexible connection hose (-FA)

-	500 mm (-FA 500)

-	800 mm (-FA 800)

-	1200 mm (-FA 1200)

-	External thread flat-sealing (WA 1/2)

-	Valves

-	Actuators

-	Control units

-	Condensation monitor

-	Air supply grille

-	PA-1-Z

-	PA-2a-Z

-	AL-1-Z

-	AL-2-Z

-	IB-1-Z

-	IB-2-Z

-	Secondary air grille

-	PA-1-A

-	IB-1-A

-	AL-1-A