Damper DKAPPs

Specification texts

Round, manually adjustable damper type DKAPPs for installation in round supply air and return air ducts for regulating the volumetric flows in air-conditioning installations. Also suitable for use with air contaminated with aggressive media.

Housing made of plastic PPs. Damper axle made of plastic PP. Plastic damper leaf and silicone-free damper leaf seal  made of PUR (NW 110 sealing airtight to DIN EN 1751 Class 2, NW 125-400 sealing airtight to DIN EN 1751 Class 3). Manual damper actuation. (Manual adjustment made of stainless steel)

Product: SCHAKO type DKAPPs

Accessories:

-	Flat flange (-FF3), on both sides, made of plastic PPs.