Damper DKG

Specification texts

Round, manually adjustable damper type DKG is suitable for installation in round supply air and return air ducts according to DIN EN 1506 for regulating the volumetric flows in air-conditioning installations. The housing and the manually adjustable damper blade consist of galvanized sheet steel fitted as standard with a rubber lip seal made of special rubber. The hand-adjustable device with position indicator and axle bearing are made of plastic. Housing leakage according to DIN EN 1751, class C (NW80 class B), at a duct pressure of up to 1000 Pa.

Product: SCHAKO type DKG