Ceiling swirl diffuser DO

Specification text

Ceiling swirl diffuser type DO-Q-... for square supply and return air models. Especially suitable for use in comfort rooms with a high air change rate and for VAV installations with variable volumetric flows (between 40 and 100%). Consisting of square sheet steel faceplate painted with a high-quality powder coating to a RAL colour (RAL 9010 (white), standard), with integrated fixed air deflection blades to produce a horizontal throw pattern, with concealed mounting (VM). For use up to -14 K. Sophisticated design allows easy cleaning to VDI 6022.

Product: SCHAKO type DO-Q-...

-	with round faceplate

Product: SCHAKO type DO-R-...

-	Front plate made of natural colour anodised aluminium (E6/EV1) (possible only with concealed mounting) (not available for DO-R-... model).

-	with screw mounting (-SM) (only DO-Q-...), only for model with ball-impact guard.

Accessories:

-	Plenum box (SK-R-10-...) made of galvanised sheet steel, with fixing lugs.

-	Supply air model with integrated perforated straightener.

-	with damper (-DK1) in plenum box, adjustable from below, for simple air volume regulation without dismounting the faceplate.

- adjustable from below with cable (-DK2)

-	with volumetric flow meter (-VME1)

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with thermal insulation

-	internal (-Ii)

-	external (-Ia)

-	height of plenum box can be freely selected, xxx in mm, (minimum height = spigot diameter + +137 mm, but at least 235 mm) (For models SK-R-10-Z-310/-400/-500-...-DK1/-DK2-...-S0, observe special height of plenum box (see p. 5))

-	Spigot diameter can be freely selected, xxx in mm

-	Spigot position:

-	S0= spigot from above

-	S1= 1 lateral spigot on the box (standard)

-	S2= 2 spigots offset by 90°

-	S3= 2 spigots offset by 180°

-	S5= 2 spigots arranged next to each other

-	Ball-impact guard (-BS), made of steel with high-quality powder coating to RAL 9010 (white), other RAL colours possible at an extra charge (available for DO-Q-... with SM mounting only).