Ceiling Diffuser DQC

Specification texts

Ceiling diffuser type DQC-Z-... for supply air consists of a square faceplate, RAL colour 9010 (white) with visible screw mounting (-SM), including four lamella fields each arranged offset by 90°. The plastic air deflection blades painted to a RAL colour similar to RAL 9005 (black, -LS9005) or RAL 9010 (white, -LW9010) are manually individually adjustable.

Product: SCHAKO type DQC-Z-...

Ceiling diffuser type DQC-A-... for exhaust air consists of a square faceplate, RAL colour 9010 (white) with visible screw mounting (-SM), including four lamella fields each arranged offset by 90° without air deflection blades.

Product: SCHAKO type DQC-A-...

Ceiling diffuser type DQC-Z-...-E013-... for supply air consists of a square faceplate, RAL colour 9010 (white) with visible screw mounting (-SM), including four lamella fields each arranged offset by 90° The plastic air deflection blades painted to a RAL colour similar to RAL 9005 (black, -LS9005) or RAL 9010 (white, -LW9010) are adjustable with an electrical servomotor at the same time.

Nominal voltage: AC 24V 50/60 Hz

Actuator signal: DC 0...10 V

Product: SCHAKO type DQC-Z-...-E013-...

Accessories:

-	Plenum box (SK-Q-16-...) made of galvanised sheet steel, with fixing lugs.

-	Supply air model with integrated perforated straightener.

-	Return air model inside painted to RAL 9005 (black)

-	with damper (-DK1) in plenum box, adjustable from below, for simple air volume regulation without 		dismounting the faceplate.

-	with volumetric flow meter (-VME1).

-	with ROB model (-ROB1), removable diffuser plate, damper and volumetric flow meter

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with thermal insulation

-	internal (-Ii)

-	external (-Ia)

-	Height of plenum box can be freely selected, xxx in mm, minimum height = spigot diameter + 124 mm, 		but at least 200 mm

-	Spigot diameter can be freely selected, xxx in mm

-	Spigot position:

-	S0 = spigot from above

-	S1 = 1 lateral spigot on the box (standard)

-	S2 = 2 spigots offset by 90°

-	S3 = 2 spigots offset by 180°

-	S5 = 2 spigots arranged next to each other

-	Ball-impact guard (-BS), made of steel painted to RAL 9010 (white), other RAL colours possible at an 	extra charge