Ceiling Diffuser DQDL

Specification texts

Ceiling diffuser type DQDL-... for supply or return air, with square faceplate. Suitable for isothermal and

cooling applications. Especially for installation in comfort rooms. Consisting of faceplate with fixed blades for

horizontal air throw and perforated edges

Product: SCHAKO type DQDL-...

Air throw:

-	Supply air (-Z)

-	Return air (-A)

Nominal size:

-	NW310 (-310)

-	NW400 (-400)

-	NW500 (-500)

-	NW600 (-600)

-	NW625 (-625)

Material:

-	Sheet steel painted with a high-quality powder coating to the RAL colour 9010 (-SB-9010, white) (standard)

-	Sheet steel painted with a high-quality powder, RAL colour can be freely selected (-SB-xxxx).

Mounting:

-	Concealed mounting (-VM) (only in combination with SK-..., not possible with ball-impact guard)

-	Screw mounting (-SM) (standard)

Accessories:

-	Plenum box (SK-Q-17-...-SV), for square air diffusers, made of galvanised sheet steel, with fixing lug

-	Model:

-	for supply air (-Z), with integrated perforated straightener.

-	for return air (-A), inside painted to black, RAL 9005.

-	Fastening:

-	Screw mounting (-SM, standard)

-	Concealed mounting (-VM), additionally with pole brace made of aluminium and pole brace holder made of plastic.

-	Height of plenum box standard (-KHS) or freely selectable (-xxx, in mm) (minimum height = spigot diameter + 102 mm, but at least 200 mm) (For SK-Q-17-Z-...-DK1/-DK2-...-S0, observe special height of plenum box (see p. 6))

-	Spigot diameter: standard (-SDS) or freely selectable (-xxx, in mm).

-	Spigot position:

-	Spigot from above (-S0)

-	1 lateral spigot (-S1) (standard)

-	2 lateral spigots, offset by 90° (-S2)

-	2 lateral spigots, offset by 180° (-S3)

-	2 spigots arranged next to each other (-S5)

-	with damper (-DK1/-DK2) in plenum box, adjustable from below, for simple air volume regulation without dismounting the faceplate.

-	with damper without cable-operated adjustment (-DK1)

-	with damper with cable-operated adjustment (-DK2)

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with volumetric flow meter (-VME1).

(not for use with a damper)

-	with ROB model (-ROB1), removable diffuser plate, damper and volumetric flow meter.

-	with thermal insulation:

-	internal (-li), inside the plenum box

-	external (-Ia), at the outside of the plenum box

-	1/4 cover (-AD), made of galvanised sheet steel.

For covering blade sections to achieve a selective air throw pattern (only possible for supply air model).

-	Ball-impact guard (-BS), made of steel with high-quality powder coating, painted to the same colour as the faceplate (RAL 9010 [white], other RAL colours possible at an extra charge) (only possible for screw mounting).