Ceiling Swirl Diffuser DQJ-SL

Specification texts

Ceiling swirl diffuser type DQJSL in round design. Particularly suitable for comfort rooms and for

VAV systems having variable volumetric flows (between 40 and 100%). Cooling and heating modes

are possible. Consisting of a perforated faceplate made of sheet steel  provided with a high-quality

powder coating in a RAL colour (RAL 9010, white, standard), with central pivoting, aerodynamic and

radial fitted deflection blades, which are individually adjustable (without any tools) from the diffuser

side without dismounting the diffuser, in support profile design made of plastic similar to RAL colour

9010 (white), RAL 9005 (black) or aluminium, painted individually or to the same RAL colour as the

faceplate (subsequent adjustment of blades not possible). Free cross-section, resistance and sound

power level constant in all blade positions. Throughput of up to 50% higher volumetric flows possible

with identical sound power and comparable size compared with swirl diffusers without perforation.

Fastening by concealed mounting (VM), made of aerodynamic aluminium profile.

Product: SCHAKO type DQJSL-Z-...

Air throw pattern:

-	increased horizontal multi-directional throw (-A)

-	high-induction horizontal multi-directional throw (only sizes 160 - 315) (-B)

-	vertical air throw (-V)

Accessories:

-	plenum box (SK-R-13-...), made of galvanised sheet steel, with fixing lugs, supply air model with integrated perforated straightener.

-	with damper (-DK1) in plenum box, adjustable from below, for simple air volume regulation without dismounting the faceplate.

-  adjustable from below with cable (-DK2)

-	with volumetric flow meter (-VME1).

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with thermal insulation

-	internal (-Ii)

-	external (-Ia)

-	Height of plenum box can be freely selected, xxx in mm, minimum height = spigot diameter +137 mm, but at least 235 mm

-	Spigot diameter can be freely selected, xxx in mm

-	Spigot position:

-	S0= spigot from above

-	S1= 1 lateral spigot on the box (standard)

-	S2= 2 spigots offset by 90°

-	S3= 2 spigots offset by 180°

-	S5 = 2 spigots arranged next to each other

-	Panelled cover plate (-PA...) made of sheet steel, painted to RAL 9010 (white), with screw mounting (-SM).