Ceiling Swirl Diffuser DQJA / DQJR

Specification texts

Ceiling swirl diffuser type DQJA-Z-..., in square design, especially for installation in grid ceilings. Especially suitable for comfort rooms up to a maximum air change rate of 12. Cooling and heating modes are possible. Consisting of a perforated faceplate made of sheet steel provided with a high-quality powder coating in a RAL colour (RAL 9010, white, standard), with central pivoting, aerodynamic radially fitted air deflection blades, which are individually adjustable, without any tools, from the diffuser front side without dismounting the diffuser, in support profile design made of plastic similar to RAL colour 9010 (white), RAL 9005 (black) or aluminium, painted individually or to the same RAL colour as the faceplate (subsequent adjustment of blades not possible). Free cross-section, resistance and sound power level constant in all blade positions. With visible screw mounting (-SM) and circumferential foam seal.

Product: SCHAKO type DQJA-Z-...

-	for return air, without air deflection blades, with square faceplate, circular punch

Product: SCHAKO type DQJA-A-...

-	for supply air, with air deflection blades, with round front plate

Product: SCHAKO type DQJR-Z-...

-	for return air without air deflection blades, with round faceplate.

Product: SCHAKO type DQJR-A-...

-	with concealed mounting (-VM), made of aerodynamic aluminium profile with 2-point suspension, only possible in connection with plenum box.

Accessories:

-	Plenum box (SK-R-12-...), made of galvanised sheet steel, with fixing lugs and lateral connection spigot. Diffuser fixing with concealed mounting (-VM)

-	Supply air model with integrated perforated straightener (-Z)

-	Return air model (-A)

-	includes a damper (-DK1) adjustable at the front side in the plenum box for air volume regulation

-	with cable-operated adjustment (-DK2)

-	with volumetric flow meter (-VME1).

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	Thermal insulation

-	internal (-Ii)

-	external (-Ia)

-	Height of plenum box can be freely selected, xxx in mm, (minimum height = spigot diameter + 137 mm, but at least 235 mm)

-	Spigot diameter can be freely selected, xxx in mm

-	Spigot position

-	S0 = spigot from above

-	S1 = 1 lateral spigot on the box (standard)

-	S2 = 2 spigots offset by 90°

- 	S3 = 2 spigots offset by 180°

-	S5 = 2 spigots arranged next to each other

-	with transition piece for flexible duct connection (-US) made of sheet steel in RAL colour 9005 (black).