Swirl diffuser DQJF

Specification texts

DQJF swirl diffuser, particularly suitable for suspended use in industrial halls, comfort rooms with high air change rates and for VAV systems with variable volumetric flows (between 40-100%). Cooling and heating modes are possible.

With round faceplate, circular blade pattern. For supply air, with central pivoting, aerodynamic radially arranged divided air deflection blades in support blade profile sections made of plastic in a colour similar to RAL 9005 (-L9005, black, standard), similar to RAL 9006 (-L9006, grey), similar to RAL 9010 (-L9010, white) or made of aluminium painted to a freely selectable RAL colour (-Axxxx, subsequent adjustment of the blades is not possible). Each blade is adjustable from the diffuser faceplate without using any special tools or dismounting the diffuser. Free cross-section, resistance and sound power level remain constant in all blade positions.

Nominal sizes: NW 500 to 800

Product: SCHAKO type DQJF-R-SR-Z-...-PT-...

-	For supply air, with central pivoting, aerodynamic radially arranged continuous air deflection blades in support blade profile sections made of plastic in a colour similar to RAL 9005 (-L9005, black, standard), similar to RAL 9006 (-L9006, grey), similar to RAL 9010 (-L9010, white) or made of aluminium painted in a RAL colour that can be freely selected (-Axxxx, subsequent adjustment of blades not possible).

Nominal size: NW 310 and NW 400

Product: SCHAKO type DQJF-R-SR-Z-...-PS-...

-	For return air, without air deflection blades.

Nominal size: NW 310 to NW 800

Product: SCHAKO type DQJF-R-SR-A...-P0-..

Faceplate:

-	Sheet steel (-SB)

-	painted to the RAL colour 9010 (white) (-9010)

-	painted to a different RAL colour, freely selectable (-xxxx) (always with 4 digits)

-	Galvanised sheet steel, without paint (-SV-0000)

-	Stainless steel V2A, painted in the colour sand silver (-V2-SAND)

Drill pattern:

-	not reduced (-000, standard)

-	reduced drill pattern:

-	drill pattern 310 (-310, NW >310)

-	drill pattern 400 (-400, NW >400)

-	drill pattern 500 (-500, NW >500)

-	drill pattern 600 (-600, NW >600)

Air throw pattern:

-	For supply air model

-	"A" (-A), all blades in position 2

-	"V" (-V), all blades in position 1 (heating mode only)

-	For return air model:

-	"C" (-C), without blades

Mounting:

-	Screw mounting (-SM) (standard)

-	sideways, by means of slotted shallow-raised countersunk-head tapping screws DIN ISO 7049 pitch 3.9 x 13 (on site)

-	Concealed mounting (-VM)

-	Pole brace fastening with an M6 cylinder screw (according to DIN EN ISO 4762) to the plenum box (-SKF).

Only possible in combination with a plenum box.

Accessories:

-	Plenum box (-SKF), in round design, with fixing lugs.

-	Type of air:

-	Supply air (-Z)

-	Return air (-A) (inside black painted to RAL colour 9005 [black])

-	Fastening:

-	Screw mounting (-SM, standard, screws must be provided on site)

-	Concealed mounting (-VM)

-	Material / paint:

-	Sheet steel (-SB)

-	painted to the RAL colour 9010 (white) (-9010).

-	painted to a different RAL colour, freely selectable (-xxxx) (always with 4 digits).

-	Galvanised sheet steel, without paint (-SV-0000)

-	Stainless steel V2A, painted in the colour sand silver (-V2-SAND)

-	Damper:

-	Without damper (-DK0) (standard).

-	With damper (-DK2), in the connection spigot, with cable-operated adjustment, made of galvanised sheet steel, adjustable, for simple air volume regulation.

-	Rubber lip seal:

-	Without rubber lip seal (-GD0)

-	with rubber lip seal (-GD1), made of special rubber, at the connection spigot.

-	Volumetric flow meter:

-	Without volumetric flow meter (-VME0) (standard).

-	With volumetric flow meter (-VME1), in the plenum box at the connection spigot. Holder made of galvanised sheet steel. Aluminium connections.

-	Insulation:

-	Without insulation (-I0)

-	With box insulation inside (-Ii), thermal insulation at the inside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS)

-	Height of plenum box in mm, can be freely selected (-xxx) (minimum height [KHS] with spigot position S1 / S2 / S3 = spigot diameter + 122 mm, but at least 220 mm, minimum height [KHS] with spigot position S0 at least 250 mm) (always with 3 digits).

-	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	Spigot diameter in mm, can be freely selected (-xxx) (always with 3 digits).

-	Spigot position:

-	1 spigot from above (-S0, standard)

-	1 lateral spigot on the box (-S1)

-	2 lateral spigots, offset by 90° (-S2)

-	2 lateral spigots, offset by 180° (-S3)

-	Cover (-A0 / -AD)

-	without cover (-A0) (standard).

-	with 1/4 cover (-AD)

-	only possible for supply air version.

-	Galvanised sheet steel

-	for 1 or 2 sided shielding.