Nozzle Jet Diffuser Model DSA

Specification texts

Nozzle jet diffuser for installation in ceilings or floors. Faceplate riveted to plenum box.

-	With fixed plastic nozzles.

Product: SCHAKO type DSA-F0-...-FV-...

-	With individually manually adjustable plastic nozzles.

Product: SCHAKO type DSA-V0-...-FV-...

Nozzle jet diffuser for installation in ceilings or floors. With dismountable faceplate. With indentations for screwed mounting (-SM, standard) of concealed mounting (-VM, traverse fixing, only possible in connection with a plenum box).

-	With fixed plastic nozzles.

Product: SCHAKO type DSA-D0-...-SM/-VM-...

-	With individually manually adjustable plastic nozzles.

Product: SCHAKO type DSA-VD-...-SM/-VM-...

Grille length:

-	600 (-00600) (DSA-F0-... / DSA-V0-...)

-	625 (-00625) (DSA-D0-... / DSA-VD-...)

-	800 (-00800) (DSA-F0-... / DSA-V0-...)

-	825 (-00825) (DSA-D0-... / DSA-VD-...)

-	1000 (-01000) (DSA-F0-... / DSA-V0-...)

-	1025 (-01025) (DSA-D0-... / DSA-VD-...)

-	1200 (-01200) (DSA-F0-... / DSA-V0-...)

-	1225 (-01225) (DSA-D0-... / DSA-VD-...)

-	Band design (-xxxxx, always with 5 digits)

-	available from BL > 1200 mm for DSA-F0-... / DSA-V0-...

-	available from BL > 1225 mm for DSA-D0-... / DSA-VD-...

Grille height

-	Nozzles 1 row (-1)

-	Nozzles 2 row (-2)

Single / band design	:

-	Single length (-N)

-	Band design (-B, two pieces and more)

-	for DSA-F0-... / DSA-V0-... available from BL >1200 mm

-	for DSA-D0-... / DSA-VD-... available from BL >1225 mm

Material / paint:

-	Sheet steel painted to RAL 9010 (-SB-9010, white, standard)

-	Sheet steel painted to RAL 9005 (-SB-9005, black)

-	Sheet steel painted to RAL colour of your choice (-SB-xxxx)

Nozzle colour:

-	white, similar to RAL colour 9010 (-DW, standard)

-	black, similar to RAL colour 9005 (-DS, standard)

-	white aluminium, similar to RAL colour 9006 (-DA)

Accessories:

-	Plenum box (-AK-30), in rectangular design. Housing with round connection spigot and fixing lugs made 	of galvanised sheet steel (-SV).

-	Fastening:

-	Permanent connection (-FV) (standard for DSA-F0-... / DSA-V0-..., not possible for DSA-D0-... / 			DSA-VD-...)

-	Screw mounting (-SM, standard, screws must be provided on site, not possible for DSA-F0-... / 			DSA-V0-...)

-	Concealed mounting (-VM, not possible for DSA-F0-... / DSA-V0-...)

-	throttle damper (-DK1) in the plenum box, adjustable at the front, made of galvanised sheet steel for 		air volume regulation.

-	rubber lip seal (-GLD1), made of special rubber, at the plenum box connection spigot

-	with thermal insulation

-	internal (-li), inside the plenum box

-	external (-la), on the outside of the plenum box (only available with already bent fixing lugs)

-	Height of plenum box:

-	Standard (-KHS)

-	Can be freely selected (-xxx, in mm) (minimum height with spigot position -S0 / -S1 = spigot 				diameter øD + 42 mm, minimum height with spigot position -S4 = spigot diameter øD + 67 mm)

-	Width of plenum box:

-	Standard (-KBS)

-	Can be freely selected (-xxx in mm) (minimum width with spigot position -S0 = spigot diameter øD 			+ 30 mm)

-	Spigot diameter:

-	Standard (-SDS)

-	Can be freely selected (-xxx, in mm)

-	Spigot position:

-	1 spigot from above (-S0)

-	1 lateral spigot on the box (-S1, standard)

-	1 spigot front side (-S4)

-	Hit-and-miss damper (-SS) made of galvanised sheet steel (only possible for DSA-D0-... and DSA-VD-...)

-	Cover sheet (-AB), made of galvanised sheet steel painted to the colour of the faceplate (only possible for 	DSA-F0-...).