Slot diffuser for plasterboard ceilings DSCL

Specification text

Highly inductive slot diffuser, free cross-section, resistance and sound power level constant in all blade positions, suitable for use in rooms with a height between 2.6 m and 4 m for direct installation in plasterboard ceilings or ceiling cavities (pressure ceilings). The special shape of the frame profile allows good installation in the plasterboard ceiling.

Slot diffuser 1-slot (-1), with 20.5 mm slot width.

Frame with frame profile PLASTER (-PL), made of extruded aluminium profile.

Frame profiles are fitted with bores to allow them to be connected to the plasterboard ceiling using screws. Mounting brackets are supplied loose as a mounting aid.

Supply air model with air deflection blades made of painted aluminium:

-	Colour similar to RAL 9010 (white) (-L9010).

-	Colour similar to RAL 9011 (graphite black, standard) (-L9011).

-	RAL colour can be freely selected (-Lxxxx, always with 5 digits).

Product: SCHAKO type DSCL-1-Z-PL-…

Return air model without air deflection blades (-00000), with perforated plate made of sheet steel painted to RAL 9011 (graphite black), as cover screen.

Product: SCHAKO type DSCL-1-A-PL-…

Frame surface:

-	Natural aluminium (-ALRO) (standard).

-	Aluminium painted to:

-	RAL colour 9010 (white) (-9010).

-	RAL colour 9011 (graphite black) (-9011).

-	a freely selectable RAL colour (-xxxx) (always with 4 digits).

Blade position for air jet:

-	without blades, for return air with perforated plate (-0).

-	with vertical throw (-V).

-	with horizontal one-way throw to the left (-L) (standard).

-	with horizontal one-way throw to the right (-R).

Length / Model:

Single design (-N)

-	Length L = 1000 mm (-N-01000).

-	Length L = 1500 mm (-N-01500).

-	Length (L) in mm, freely selectable (-N-xxxxx, always with 5 digits).

(can be fitted with a plenum box in case of single design lengths L = ≥400 mm to ≤1500 mm).

Band design (-B)

-	Length in mm, as band (-B-xxxxx).

(Available lengths according to SCHAKO standard) with connecting pins, supplied loose (2 for each connection).

Mounting:

-	without box mounting (-OM) (standard).

Ceiling depth of plaster board:

-	Ceiling depth T = 9.5 mm (-095).

-	Ceiling depth T = 12.5 mm (standard) (-125).

-	Ceiling depth (T) can be freely selected (-xxx, always with 3 digits).

End piece (-EP/-EB):

-	With surrounding edge for plastering, mounted ex-works on both sides (-EP) (standard).

-	made of galvanised sheet steel, painted to the RAL colour of the frame profile.

-	straight, mounted ex works on both sides (-EB).

-	made of galvanised sheet steel, painted to the RAL colour of the frame profile.

In the band design, the end piece is mounted to the left side of the section (left TS) and to the right side of the difference in length (DL) as a standard.

Accessories:

-	Plenum box (-ASK-72) with air diffuser plate made of galvanised sheet steel (-SV), for 1-slot models
(-1), with mounting brackets, suspension without riveting nut (-E0).

-	Single / band design:

-	Single design (-N, length of box KL max. 1500 mm).

-	Band design (-B, available lengths according to SCHAKO standard for band design).

-	Length:

-	length L = 1000 mm (-01000)

(length of box KL=1000 mm).

-	length L = 1500 mm (-01500)

(length of box KL=1500 mm).

-	Length (L/BL) in mm, freely selectable (-xxxxx, always with 5 digits) (length of box KL = L / total length of box GKL = BL).

-	Mounting of box:

-	Without diffuser mounting (-OM) (standard).

-	Damper:

-	Without damper (-DK0) (standard).

-	With damper and cable-operated adjustment (-DK2), made of galvanised sheet steel, in the connection spigot, adjustable, for simple air volume regulation.

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.

-	Insulation:

-	without insulation (-I0) (standard).

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS).

-	Height of plenum box in mm, freely selectable (-xxx) (always with 3 digits) (minimum height of plenum box with spigot position S1+S4 = spigot diameter øD + 82 mm / with spigot position S0 = 230 mm).

-	Spigot position:

-	Spigot from above (-S0).

-	Lateral spigot (-S1, standard).

-	Spigot front side (-S4) (not possible for band design).

-	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	Spigot diameter (øD) in mm, freely selectable (-xxx, always with 3 digits).

-	Dummy piece (-BS0 / -BS1)

-	without dummy piece (-BS0) (standard).

-	with dummy piece (-BS1):

-	made of sheet steel painted to RAL colour 9011 (graphite black).

-	possible from length L ≥ 200 mm.

-	only possible without plenum box ASK-72.

-	Corner angle (-EW-72), 1-slot model (-1), with 20.5 mm slot width. Frame with frame profile PLASTER (-PL), made of extruded aluminium profile. With 4 fishplates (-VL, included in delivery) made of aluminium (same colour as frame), supplied loose.

Frame profiles are fitted with bores to allow them to be connected to the plasterboard ceiling using screws. Mounting brackets are supplied loose as a mounting aid.

-	Frame surface made of:

-	Natural aluminium (-ALRO) (standard).

-	Aluminium painted to:

-	RAL colour 9010 (white) (-9010).

-	RAL colour 9011 (graphite black) (-9011).

-	a freely selectable RAL colour (-xxxx, always with 4 digits).

-	Dummy plate colour, made of painted sheet steel:

-	colour similar to RAL 9010 (white) (-B9010).

-	colour similar to RAL 9011 (graphite black) (-B9011) (standard).

-	a freely selectable RAL colour (Bxxxx) (always with 5 digits).

-	Angle between sides:

-	angle  = 90° (-090).

-	angle () as required (-xxx, always with 3 digits)

Angle values between a = 90° (-090, standard) and 170° (-170) are possible.

-	Left-side length (a):

-	Standard length L=250 (-000).

-	Length (L) in mm, freely selectable (-xxx, always with 3 digits) (minimum length = standard length).

-	Right-side length (b):

-	Standard length L=250 (-000).

-	Length (L) in mm, freely selectable (-xxx, always with 3 digits) (minimum length = standard length).

-	Ceiling depth of plaster board:

-	Ceiling depth T = 9.5 mm (-095).

-	Ceiling depth T = 12.5 mm (-125) (standard).

-	Ceiling depth (T) can be freely selected (-xxx, always with 3 digits).