Curved slot diffuser for plasterboard ceilings DSCP

Specification text

Highly inductive curved slot diffuser, free cross-section, resistance and sound power level constant in all blade positions, suitable for use in rooms with a height between 2.6 m and 4 m for direct installation in plasterboard ceilings or ceiling cavities (pressure ceilings). The special shape of the frame profile allows good installation in the plasterboard ceiling.

Frame with frame profile PLASTER (-PL), made of extruded aluminium profile.

Frame profiles are fitted with bores to allow them to be connected to the plasterboard ceiling using screws. Mounting brackets are supplied loose as a mounting aid.

Supply air model with pivoting air deflection blades in support profile shape made of plastic material (hard PVC):

-	Colour similar to RAL 9005 (black, standard) (-L9005)

-	Colour similar to RAL 9010 (white) (-L9010)

-	Freely selectable RAL colour (-Lxxxx, always with 5 digits)

Product: SCHAKO type DSCP-…-Z-PL-...

Return air model without air deflection blades (-00000), with perforated plate made of sheet steel painted to RAL 9005 (black), as cover screen.

Product:: SCHAKO type DSCP-…-A-PL-…

| Volumetric flows in m³/h per m at: | 35 dB(A) | 40 dB(A) |
| --- | --- | --- |
| DSCP-1 | 131 | 156 |
| DSCP-2 | 203 | 242 |

Model (number of slots)

-	1-slot (-1)

-	2-slot (-2)

Frame surface:

-	consisting of:

-	natural aluminium (-ALRO) (standard)

-	Aluminium painted to:

-	RAL colour 9005 (-9005) (black)

-	a freely selectable RAL colour (-xxxx, always with 4 digits).

-	central partition (only for 2-slot models):

-	for supply air:

-	for frame made of natural aluminium, same RAL colour as the blade.

-	for painted frame made of aluminium, same RAL colour as the frame.

-	for return air, made of aluminium painted to RAL 9005 (black).

Blade position for air jet:

-	without blades, for return air, with perforated plate (-0).

-	With vertical throw (-V)

-	With horizontal one-way throw toward the inside (-L)

-	With horizontal one-way throw toward the outside (-R)

-	with horizontal two-way throw (-B) (standard)

Curved length / model:

Single design (-N)

-	curved length BoL = 1000 mm (-N-01000)

(curved length of box KBoL = 1000 mm)

-	curved length BoL = 1500 mm (-N-01500) (curved length of box KBoL = 1500 mm)

-	Curved length (BoL) in mm, freely selectable (-N-xxxxx, always with 5 digits) (In case of single design with curved length BoL = ≥500 mm to <1500 mm can be fitted with a plenum box).

Band design (-B)

-	curved length (BBoL) in mm, freely selectable, as band (-B-xxxxx)

Curved length distribution according to SCHAKO standard lengths for band design. With connecting pins, supplied loose (2 for each connection).

Radius:

-	≥ 2,000 mm (-XXXXX, always with 5 digits)

Mounting:

-	without box mounting (-OM) (standard)

Ceiling depth of plaster board:

-	ceiling depth T = 9.5 mm (-095)

-	ceiling depth T = 12.5 mm (standard) (-125)

-	ceiling depth (T) freely selectable (-xxx, always with 3 digits)

End piece (-EP/-EB):

-	with surrounding edge for plastering, mounted ex works on both sides (-EP) (standard).

-	made of galvanised sheet steel

-	straight, mounted ex works on both sides (-EB).

-	made of galvanised sheet steel

In the band design, the end piece is mounted to the left side of the section (left TS) and to the right side of the difference in curved length (DBoL) as a standard.

Accessories:

-	Plenum box (-ASK-46), made of galvanised sheet steel (-SV), with mounting brackets, without riveting nut (-E0), with air diffuser plate, made of galvanised sheet steel.

-	Model (number of slots):

-	1-slot (-1)

-	2-slot (-2)

-	Single / band design:

-	single design (-N, curved length of box KBoL max. 1500 mm)

-	band design (-B, curved length distribution according to SCHAKO standard lengths for band design)

-	Curved length:

-	curved length BoL = 1000 mm (-01000)

(curved length of box KBoL = 1000 mm)

-	curved length BoL = 1500 mm (-01500)

(curved length of box KBoL = 1500 mm)

-	curved length (BoL/BBoL) in mm, freely selectable (-xxxxx, always with 5 digits) (curved length of box KBoL = BoL / total curved length of box GKBoL = BBoL).

-	Radius:

-	specify a radius R = ≥2000 mm (-xxxxx, always with 5 digits)

-	Mounting of box:

-	without diffuser mounting (-OM) (standard)

-	Damper:

-	without damper (-DK0) (standard)

-	With damper and cable-operated adjustment (-DK2), made of galvanised sheet steel, in the connection spigot, adjustable, for simple air volume regulation.

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard)

-	with rubber lip seal (-GD1), made of special rubber, at the connection spigot.

-	Insulation:

-	without insulation (-I0) (standard)

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	standard height of box (-KHS)

-	Height of box (KHS) in mm, freely selectable (-xxx) (always with 3 digits) (minimum height of box [KHS] with spigot position S1+S2 = spigot diameter øD + 82 mm / with spigot position S0 = 220 mm).

-	Spigot position:

-	spigot from above (-S0)

-	inner lateral spigot (-S1) (standard)

-	outer lateral spigot (-S2)

-	Spigot diameter:

-	standard spigot diameter (-SDS)

-	spigot diameter (øD) in mm, freely selectable (-xxx, always with 3 digits).

-	Dummy piece (-BS0/-BS1):

-	without dummy piece (-BS0) (standard)

-	with dummy piece (-BS1):

-	made of sheet steel painted to RAL colour 9005 (black).

-	possible from curved length BoL ≥ 200 mm.

-	only possible without plenum box ASK-46.

-	with fastening clips for mounting on the slot diffuser.