Slot diffuser for plasterboard ceilings DSCPL

Specification text

Highly inductive slot diffuser, free cross-section, resistance and sound power level constant in all blade positions, suitable for use in rooms with a height between 2.6 m and 4 m for direct installation in plasterboard ceilings or ceiling cavities (pressure ceilings). The special shape of the frame profile allows good installation in the plasterboard ceiling.

Frame with frame profile PLASTER (-PL), made of extruded aluminium profile.

Frame profiles are fitted with bores to allow them to be connected to the plasterboard ceiling using screws. Mounting brackets are supplied loose as a mounting aid.

Supply air model with pivoting air deflection blades in support profile shape made of plastic material (hard PVC):

-	Colour similar to RAL 9005 (black, standard) (-L9005).

-	Colour similar to RAL 9010 (white) (-L9010).

-	Freely selectable RAL colour (-Lxxxx, always with 5 digits).

Product: SCHAKO type DSCPL-…-Z-PL-…

Return air model without air deflection blades (-00000), with perforated plate made of sheet steel painted to RAL 9005 (black), as cover screen.

Product: SCHAKO type DSCPL-…-A-PL-…

Model (number of slots)

-	1-slot (-1)

-	2-slot (-2)

Frame surface:

-	made of:

-	natural aluminium (-ALRO) (standard).

-	Aluminium painted to:

-	 RAL colour 9005 (-9005) (black).

-	a freely selectable RAL colour (-xxxx, always with 4 digits).

-	central partition (only for 2-slot models):

-	for supply air

-	for frame made of natural aluminium, same RAL colour as the blade.

-	for painted frame made of aluminium, same RAL colour as the frame.

-	for return air, made of aluminium painted to RAL 9005 (black).

Blade position for air jet:

-	without blades, for return air, with perforated plate (-0).

-	with vertical throw (-V).

-	with horizontal one-way throw to the left (-L).

-	with horizontal one-way throw to the right (-R).

-	with horizontal two-way throw (-B) (standard).

Length / Model:

Single design (-N)

-	length L= 1000 mm (-N-01000)

(length of box KL = 1000 mm)

-	length L= 1500 mm (-N-01500)

(length of box KL = 1500 mm)

-	length (L) in mm, freely selectable (-N-xxxxx, always with 5 digits)

(length of box KL = L, can be fitted with a plenum box in case of single design lengths L = ≥400 mm to ≤1500 mm.)

Band design (-B)

-	Length in mm, as band (-B-xxxxx)

(available lengths according to SCHAKO standard for band design) (total length of box GKL = BL, with connecting pins, supplied loose (2 for each connection).

Mounting:

-	without box mounting (-OM) (standard).

Ceiling depth of plaster board:

-	Ceiling depth T = 9.5 mm (-095).

-	Ceiling depth T = 12.5 mm (standard) (-125).

-	Ceiling depth (T) can be freely selected (-xxx, always with 3 digits).

End piece (-EP/-EB):

-	with surrounding edge for plastering, mounted ex-works on both sides (-EP) (standard)

-	made of galvanised sheet steel.

-	straight, mounted ex works on both sides (-EB)

-	made of galvanised sheet steel.

In the band design, the end piece is mounted to the left side of the section (left TS) and to the right side of the difference in length (DL) as a standard.

Accessories:

-	Plenum box (-ASK-25), made of galvanised sheet steel (-SV), with mounting brackets, without riveting nut (-E0), with air diffuser plate, made of galvanised sheet steel.

-	Model:

-	1-slot (-1).

-	2-slot (-2).

-	Single / band design:

-	Single design (-N, length of box KL max. 1500 mm).

-	Band design (-B, available lengths according to SCHAKO standard for band design).

-	Length:

-	1000 mm (-01000) (length of box KL=1000 mm).

-	1500 mm (-01500) (length of box KL=1500 mm).

-	Length (L/BL) in mm, freely selectable (-xxxxx, always with 5 digits) (length of box KL = L / total length of box GKL = BL).

-	Mounting of box:

-	Without diffuser mounting (-OM) (standard).

-	Damper:

-	Without damper (-DK0) (standard).

-	With damper and cable-operated adjustment (-DK2), made of galvanised sheet steel, in the connection spigot, adjustable, for simple air volume regulation.

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.

-	Insulation:

-	without insulation (-I0) (standard).

-	With box insulation outside (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS).

-	Height of plenum box (KHS) in mm, freely selectable (-xxx) (always with 3 digits) (minimum height of plenum box [KHS] with spigot position S1+S4 = spigot diameter øD + 82 mm / with spigot position S0 = 220 mm).

-	Spigot position:

-	Spigot from above (-S0).

-	Lateral spigot (-S1) (standard).

-	Spigot front side (-S4) (not possible for band design).

-	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	Spigot diameter (øD) in mm, freely selectable (-xxx).

-	Dummy piece (-BS0/-BS1):

-	without dummy piece (-BS0) (standard).

-	with dummy piece (-BS1):

-	made of sheet steel painted to RAL colour 9005 (black).

-	possible from length L ≥ 200 mm.

-	only possible without plenum box ASK-25 and hit-and-miss damper.

-	with fastening clips for mounting on the slot diffuser.

-	Corner angle (-EW-25), frame with frame profile PLASTER (-PL), made of extruded aluminium profile. With 4 fishplates (-VL, included in delivery) made of aluminium (same colour as frame), supplied loose.

Frame profiles are fitted with bores to allow them to be connected to the plasterboard ceiling using screws. Mounting brackets are supplied loose as a mounting aid.

-	Model (number of slots):

-	1-slot (-1).

-	2-slot (-2).

-	Frame surface:

-	made of:

-	natural aluminium (-ALRO) (standard).

-	Aluminium painted to:

-	RAL colour 9005 (-9005) (black).

-	a freely selectable RAL colour (-xxxx, always with 4 digits).

-	central partition (only for 2-slot models):

-	for supply air:

-	for frame made of natural aluminium, same RAL colour as the blade.

-	for painted frame made of aluminium, same RAL colour as the frame.

-	for return air, made of aluminium painted to RAL 9005 (black).

-	dummy profile colour, made of painted aluminium:

-	colour similar to RAL 9005 (black) (-B9005) (standard).

-	colour similar to RAL 9010 (white) (-B9010).

-	to a freely selectable RAL colour (Bxxxx, always with 5 digits).

-	Angle between sides:

-	Angle  = 90° (-090) (standard).

-	angle () as required (-xxx, always with 3 digits)

Angle values between a = 90° (-090, standard) and 170° (-170) are possible.

-	Left-side length (a):

-	Standard length L=250 (-000)

-	Length (L) in mm, freely selectable (-xxx, always with 3 digits) (minimum length = standard length).

-	Right-side length (b):

-	Standard length L=250 (-000)

-	Length (L) in mm, freely selectable (-xxx, always with 3 digits) (minimum length = standard length).

-	Ceiling depth of plaster board:

-	Ceiling depth T = 9.5 mm (-095).

-	Ceiling depth T = 12.5 mm (-125) (standard).

-	Ceiling depth (T) can be freely selected (-xxx, always with 3 digits).

-	hit-and-miss damper (-SN/-SS)

-	without hit-and-miss damper (-SN) (standard).

-	with hit-and-miss damper (-SS):

-	made of electrolytically galvanised sheet steel.

-	only possible without plenum box ASK-25.

-	with fastening clips for mounting on the slot diffuser.