Curved slot diffuser DSCU

Specification text

Highly inductive curved slot diffuser, free cross-section, resistance and sound power level constant in all blade positions.

Supply air model with pivoting air deflection blades in support profile shape made of plastic material (hard PVC):

-	Colour similar to RAL 9005 (black, standard) (-L9005).

- 	Colour similar to RAL 9006 (white aluminium) (-L9006).

-	Colour similar to RAL 9010 (white) (-L9010).

-	painted to a freely selectable RAL colour (-Lxxxx, always with 5 digits).

Product: SCHAKO type DSCU-…-Z-…

Return air model without air deflection blades (-00000), with perforated plate made of sheet steel painted to RAL 9005 (black), as cover screen.

Product: SCHAKO type DSCU-…-A-…

Model (number of slots):

-	1-slot (-1)

-	2-slot (-2)

-	3-slot (-3)

Frame profile:

-	STANDARD frame profile (-R0)

Frame surface:

-	Natural colour anodised aluminium (standard, -ELOX)

-	Aluminium painted to:

-	RAL colour 9006 (white aluminium) (-9006).

-	RAL colour 9010 (white) (-9010).

-	a different RAL colour, freely selectable (-xxxx) (always with 4 digits).

Blade position for air jet:

- 	without blades, for return air, with perforated plate (-0)

- 	with vertical throw (-V)

- 	with horizontal one-way throw to the left (-L)

- 	with horizontal one-way throw to the right (-R)

- 	with horizontal two-way throw (-B) (standard)

Curved length / model:

Single design (-N)

- 	curved length BoL = 1000 mm (-N-01000)

- 	curved length BoL = 1500 mm (-N-01500)

- 	Curved length (BoL) in mm, freely selectable (-N-xxxxx, always with 5 digits) (In case of single design with curved length BoL = ≥ 400 mm to ≤ 1500 mm can be fitted with a plenum box.)

Band design (-B)

- 	Curved length (BBoL) in mm, as band (-B-xxxxx)

(Curved length distribution according to SCHAKO standard, with connecting pins, supplied loose (2x for each connection).

Radius:

- 	Radius >2000 mm (-xxxxx, always with 5 digits)

Mounting:

-	Permanent connection with plenum box (-FV)

-	Only possible with plenum box (-ASK-45).

-	The slot diffuser is permanently connected to the plenum box.

-	Mounting with clamp strap (-KB)

-	Only possible without plenum box.

-	Screws and clamp straps are supplied loose.

-	The slot diffuser is screwed to the clamp strap with concealed screws (included in delivery).

-	For mounting, access on the rear is not required!

Accessories:

-	End pieces (-E0 / -ES / -EB / -EL / -ER)

-	without end piece (-E0) (standard).

-	with end pieces, made of aluminium (same colour as frame):

-	Supplied loose (-ES, pair) (standard).

-	Mounted ex works on both sides (-EB).

-	Mounted ex works on the left side (-EL).

-	Mounted ex works on the right side (-ER).

-	Dummy piece (-BS0 / -BS1)

-	without dummy piece (-BS0) (standard).

-	with dummy piece (-BS1):

-	made of sheet steel painted to RAL 9005 (black).

-	Only possible without plenum box.

-	with fastening clips for mounting on the slot diffuser.

-	   possible from curved length BoL ≥ 200 mm.

-	Mounting only possible with clamp strap (-KB).

-	Plenum box (-ASK-45), with mounting brackets.

-	Model (number of slots):

-	1-slot (-1)

-	2-slot (-2)

-	3-slot (-3)

-	Single / band design:

-	single design (-N, curved length of box KBoL max. 1500 mm).

-	Band design (-B, curved length distribution according to SCHAKO standard lengths for band design).

-	Curved length:

-	curved length BoL = 1000 mm (-01000) (KBoL = 997 mm)

-	curved length BoL = 1500 mm (-01500) (KBoL = 1497 mm)

-	curved length (BoL / KBoL) in mm, freely selectable (-xxxxx, always with 5 digits)

(Curved length of box KBoL = BoL-3 / total curved length of box GKBoL = BBoL-3, in case of single design with curved length BoL = ≥ 400 mm to ≤ 1500 mm can be fitted with a plenum box).

-	Radius:

-	specify a radius ≥ 2000 mm (-xxxxx, always with 5 digits)

-	   Mounting of box:

-	   Permanent connection (-FV) (standard).

-	Material:

-	   Galvanised sheet steel (-SV) (standard).

-       Damper:

-	     without damper (-DK0) (standard)

-	     With damper (-DK1) made of galvanised sheet steel, adjustable, for simple air volume regulation

in the plenum box housing.

-	 Rubber lip seal:

-	     without rubber lip seal (-GD0) (standard)

-	  with rubber lip seal (-GD1), made of special rubber, at the connection spigot.

- 	     Insulation:

-	     without insulation (-I0) (standard)

-	  with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	 Height of plenum box:

- 	     standard height of box (-KHS)

-	   height of box in mm, freely selectable (-xxx, always with 3 digits) (minimum height [GH] for

spigot position S1+S2 = spigot diameter øD + 82 mm).

-	 Spigot position:

-	     inner lateral spigot (-S1) (standard)

-	     outer lateral spigot (-S2)

-	Spigot diameter:

-	     standard spigot diameter (-SDS)

-	  Spigot diameter (øD) in mm, freely selectable (-xxx, always with 3 digits).

-	Suspension:

-	     without riveting nut (-E0) (standard)

-	     With riveting nut (-EM), made of brass.