Slot diffuser DSCXLS

Specification text

Highly inductive slot diffuser, free cross-section, resistance and sound power level constant in all blade positions, suitable for use in rooms with a height between 2.6 m and 4 m.

Slot diffuser model (number of slots) 1-slot (-1), with slot width 30 mm.

Supply air model with air deflection blades made of painted aluminium:

-	RAL colour 9010 (white) (-L9010).

-	RAL colour 9011 (graphite black, standard)

(-L9011).

-	to another RAL colour, freely selectable (-Lxxxx, always 5 digits)

With connecting bridge made of plastic material, colour similar to RAL 9005 (black).

Product: SCHAKO Type DSCXLS-1-Z-…

Return air model without air deflection blades (-00000), with perforated plate made of painted sheet steel RAL 9011 (graphite black) (FQ = 46 %), as cover screen.

With connecting bridge made of galvanised sheet steel.

Product: SCHAKO Type DSCXLS-1-A-...

Frame made of extruded aluminium profile, consisting of:

-	Frame profile:

-	Frame profile Standard (-R0, with support profile), for visible installation on the ceiling.

-	Frame surface:

-	natural colour anodised (-ELOX, standard).

-	painted to the colour RAL 9010 (white, -9010).

-	painted to RAL colour 9011 (graphite black, -9011).

-	painted to another RAL colour, freely selectable (-xxxx, always 4 digits).

Blade position for air jet:

-	without blades, for return air (-0).

-	Blades with vertical throw (-V).

-	Blades with horizontal one-way throw to the left (-L, standard).

-	Blades with one-way horizontal throw to the right (-R).

Length / Model:

Single design (-N)

-	1000 mm (-N-01000).

-	1500 mm (-N-01500).

-	Length in mm, can be freely selected (-N-xxxxx, always with 5 digits).

(Length L ≥400 mm to ≤1500 mm can be fitted with plenum box, dummy piece possible from length 200 mm)

Band design (-B)

-	Length in mm, as band (-B-xxxxx).

Available lengths according to SCHAKO standard for band design.

Individual elements length max. 1500 mm.

With fishplates made of aluminium sheet, supplied loose (2 for each connection).

Mounting:

-	without connection (-00)

-	Only possible without plenum box.

-	Permanent connection with plenum box (-FV)

-	Only possible with plenum box.

-	Only for return and supply air model.

-	The slot diffuser is permanently connected to the plenum box.

- Concealed mounting with plenum box (-VM)

-	Only possible with plenum box.

-	Only for return and supply air model.

-	The slot diffuser is screwed to the pole brace in the plenum box housing with concealed screws.

-	Frame with foam gasket.

-	Plenum box mounted ex works.

-	Mounting with counter pole brace (-GT)

-	Only possible without plenum box.

-	Screws and pole brace traps are supplied loose (2 pieces).

-	Pole brace traps consisting of folded galvanised sheet steel and pole brace made of extruded aluminium profile with DIN thread.

-	The slot diffuser is screwed to the counter pole brace (pole brace strap) with concealed screws (included in delivery).

-	For mounting, access on the rear is required!

-	Mounting with clamp strap (-KB)

-	Only possible without plenum box.

-	Screws and clamp straps are supplied loose (2 pieces).

-	Clamp strap made of galvanised sheet steel.

-	The slot diffuser is screwed to the clamp strap with concealed screws (included in delivery).

-	For mounting, access on the rear is not required!

-	Mounting with suspension lugs (-AL)

-	Only possible without plenum box.

-	4 pieces, supplied loose and not folded.

-	The slot diffuser is fastened to 4 suspension brackets.

-	Suspension lug made of galvanised sheet steel, with holes for hook mounting.

Accessories:

-	End pieces

-	without end piece (-E00).

-	End piece models:

-	End piece, straight, made of galvanised sheet steel, painted to RAL colour of the frame profile:

-	Supplied loose (-ES1, pair) (standard).

-	Mounted ex works on both sides (-EB1).

-	Mounted ex works on the left side (-EL1).

-	Mounted ex works on the right side (-ER1).

-	Angle end piece, made of extruded aluminium profile, painted in the RAL colour of the frame profile.

-	Supplied loose (-ES2, pair) (standard).

-	Mounted ex works on both sides (-EB2).

-	Mounted ex works on the left side (-EL2).

-	Mounted ex works on the right side (-ER2).

-	Dummy piece

-	Without dummy piece (-BS0).

-	with dummy piece (-BS1), made of sheet steel painted to RAL 9011 (graphite black). Mounting only possible with counter pole brace (-GT) or clamp strap (-KB) (possible starting from length L = 200 mm, only without plenum box).

-	Plenum box (-ASK-28), for DSCXLS, model (number of slots) 1-slot (-1), made of galvanised sheet steel (-SV, standard), with suspension lugs.

-	Single / band design:

-	Single design (-N, length of box max. 1500 mm)

-	Band design (-B, available lengths according to SCHAKO standard for band design)

-	Length:

-	1000 mm (-01000)

-	1500 mm (-01500)

-	Length in mm, can be freely selected (-xxxxx, always with 5 digits)

(length min. 400 mm / max. 1500 mm).

-	Mounting of box:

-	Permanent connection (-FV) (standard).

-	Concealed mounting (-VM).

-	Damper:

-	without damper (-DK0) (standard).

-	with damper and cable-operated adjustment (-DK2), made of galvanised perforated plate (FQ = 36 %), in the connection spigot, adjustable, for simple air volume regulation.

-	Rubber lip seal:

-	Without rubber lip seal (-GD0).

-	With rubber lip seal (-GD1) made of special rubber, at the connection spigot.

-	Insulation:

-	Without insulation (-I0)

-	With box insulation inside (-Ii), thermal insulation at the inside of the plenum box.

-	With box insulation outside (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS).

-	Height of plenum box in mm, freely selectable (-xxx) (minimum height [KHS] = spigot diameter + 82 mm, always with 3 digits).

-	Box neck extension:

-	Standard box neck (-KVS).

-	Box neck extension in mm, freely selectable (-xxx) (possible from >45 mm to 200 mm).

-	Spigot position:

-	Spigot from above (-S0).

-	Lateral spigot (-S1) (standard).

-	Lateral spigot located on the opposite side (-S2).

-	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	Spigot diameter in mm, freely selectable (-xxx, always with 3 digits).

-	Suspension:

-	Without riveting nut (-E0).

-	With riveting nut (-EM), made of brass.

-	with air diffuser plate (FQ = 46 %), made of galvanised perforated plate, for even distribution of the air flow (to stabilize the pressure in the plenum box).

-	Corner angle (-EW-28), for DSCXLS, model (number of slots) 1-slot (-1) with slot width 30 mm, with standard frame profile (-R0, with support profile, for visible installation on the ceiling).

-	frame surface, made of extruded aluminium profile:

-	natural colour anodised (-ELOX, standard).

-	painted to the colour RAL 9010 (white) (-9010).

-	painted to RAL colour 9011 (graphite black) (-9011).

-	painted to another RAL colour, freely selectable (at an extra charge) (-xxxx).

-	Connecting bridge made of galvanised sheet steel, fastened by means of rivets.

-	Colour of cover plate:

-	Sheet steel painted to RAL colour 9005 (black) (-B9010) (standard).

-	Sheet steel painted to RAL colour 9010 (white) (-B9010).

-	Sheet steel painted to another RAL colour, freely selectable (Bxxxx).

-	Angle between sides:

-	90° (-090).

-	Angle as required (-xxx), values between a = 90° (-090, standard) and 170° (-170) are possible.

-	Left-side length (a):

-	Standard length L = 250 mm (-000).

-	Length can be freely selected (-xxx) (minimum length = standard length).

-	Right-side length (b):

-	Standard length L = 250 mm (-000).

-	Length can be freely selected (-xxx) (minimum length = standard length).

-	Including 4 fishplates (-VL, included in delivery) made of aluminium (same colour as frame), supplied loose.

-	Mounting:

-	with counter pole brace (-GT), screws and pole brace traps are supplied loose (2 pieces).

-	with clamp strap (-KB), screws and clamp straps are supplied loose (2 pieces).

-	with suspension lugs (-AL), supplied loose and not folded, 4 pieces.