Wall Slot Diffuser DSX-XXL-W

Specification texts

The wall slot diffuser type DSX-XXL-W-S for supply air is a narrow version with a narrow frame profile suitable for installation in walls. The high induction ensures fast reduction of the air outflow velocity and of the temperature difference.

Slot diffuser consisting of extruded aluminium profile painted in black (RAL 9005) or white (RAL 9010), depending on the colour of the air guide blade.

Air guide element made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Product: SCHAKO type DSX-XXL-W-S-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	Air guide element position

-	LV, air throw diagonally upwards

-	Length:

-	400 mm

-	500 mm

-	600 mm

-	800 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-		Return air version with air guide elements

Product: SCHAKO type DSX-XXL-W-S-A

Accessories:

-	with plenum box (-ASK-W) made of galvanised sheet steel, as well as lateral connection spigot and 		fixing lugs.

-	with a throttle damper (-DK) in the connection spigot adjustable from the front for air volume

regulation.

-	with rubber lip seal (-GD)

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	with M4 riveting nuts

-	with end piece (-ES1) (supplied loose as standard), made of painted aluminium

-	RAL 9005 (black) or

-	RAL 9010 (white)

Wall slot diffuser type DSX-XXL-W-P for supply air is a narrow version with a frame profile, suitable for installation in walls. The high induction ensures fast reduction of the air outflow velocity and of the temperature difference.

Slot diffuser made of extruded aluminium profiles in natural colour anodised E6/EV1 or painted to RAL 9010 (white).

Air guide blades made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Product: SCHAKO type DSX-XXL-W-P-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	Air guide element position

-	LV, air throw diagonally upwards

-	Length:

-	400 mm

-	500 mm

-	600 mm

-	800 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-		Return air version with air guide elements

Product: SCHAKO type DSX-XXL-W-P-A

Accessories:

-	with plenum box (-ASK-W) made of galvanised sheet steel, as well as lateral connection spigot and 		fixing lugs.

-	with a throttle damper (-DK) in the connection spigot adjustable from the front for air volume

regulation.

-	with rubber lip seal (-GD)

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	with M4 riveting nuts

-	with end piece (-ES2) (supplied loose as standard)

-	Natural colour anodised aluminium (E6/EV1)

-	aluminium painted in white (RAL 9010)

The wall slot diffuser type DSX-XXL-W-PA for supply air has a U-frame profile suitable for installation in walls. The high induction ensures fast reduction of the air outflow velocity and of the temperature difference.

Slot diffuser made of extruded aluminium profiles in natural colour anodised E6/EV1 or painted to RAL 9010 (white).

Air guide element made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Product: SCHAKO type DSX-XXL-W-PA-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	Air guide element position

-	LV, air throw diagonally upwards

-	Length:

-	400 mm

-	500 mm

-	600 mm

-	800 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-		Return air version with air guide elements

Product: SCHAKO type DSX-XXL-W-PA-A

Accessories:

-	with plenum box (-ASK-W) made of galvanised sheet steel, as well as lateral connection spigot and 		fixing lugs.

-	with a throttle damper (-DK) in the connection spigot adjustable from the front for air volume

regulation.

-	with rubber lip seal (-GD)

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	with M4 riveting nuts

The wall slot diffuser type DSX-XXL-W-PB for supply air is a narrow version with a wide frame profile, suitable for installation in walls. The high induction ensures fast reduction of the air outflow velocity and of the temperature difference.

Slot diffuser made of extruded aluminium profiles in natural colour anodised E6/EV1 or painted to RAL 9010 (white).

Air guide element made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Product: SCHAKO type DSX-XXL-W-PB-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	Air guide element position

-	LV, air throw diagonally upwards

-	Length:

-	400 mm

-	500 mm

-	600 mm

-	800 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	 for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-		Return air version with air guide elements

Product: SCHAKO type DSX-XXL-W-PB-A

Accessories:

-	with a plenum box (-ASK-W) made of galvanised sheet steel, a lateral connection spigot and 		fixing lugs.

-	with a throttle damper (-DK) in the connection spigot adjustable from the front

for air volume regulation.

-	with rubber lip seal (-GD)

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	with M4 riveting nuts

-	with end piece (-ES3) (supplied loose as standard)

-	Natural colour anodised aluminium (E6/EV1)

-	aluminium painted in white (RAL 9010)