Ceiling Slot Diffuser DSX-XXL

Specification texts

Ceiling slot diffuser type DSX-XXL-S, for supply air, suitable for installation in closed ceiling systems or for invisible installation in the joint of panelled ceilings. Air outflow direction can be adjusted afterwards from below. Noise level and pressure loss remain constant in all air guide blade positions.

Slot diffuser consisting of extruded aluminium profile painted in black (RAL 9005) or white (RAL 9010), depending on the colour of the air guide blade.

Air guide element made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Volumetric flows in m³/h at:	35 dB(A)		40 dB(A)

DSX-XXL-S-1 				172			216

DSX-XXL-S-2				293			344

DSX-XXL-S-3 				425			498

DSX-XXL-S-4 				492			581

Product: SCHAKO type DSX-XXL-S-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	3 (3-slot)

-	4 (4-slot)

-	 Air guide element position:

-	L II L, one-way horizontal throw on the left

-	L II R, one-way horizontal throw on the right

-	L III, mutual horizontal outflow (standard)

-	Length:

-	500 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-	Return air version with air guiding blades

Product: SCHAKO type DSX-XXL-S-A

Accessories:

-	with galvanised sheet steel plenum box (-ASK), and lateral connection spigot and fixing lugs.

-	with a throttle damper (-DK) in the connection spigot adjustable from the front for air volume

regulation.

-	with rubber lip seal (-GD)

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	with M4 riveting nuts

-	with end piece (-ES1) (supplied loose as standard), made of painted aluminium

-	RAL 9005 (black) or

-	RAL 9010 (white)

-	Corner bracket 90° (-EW) (supplied loose as standard)

Ceiling slot diffuser type DSX-XXL-P, for supply air, with support profile for installation in ceiling panels, suitable for installation in closed ceiling systems. Air outflow direction can be adjusted afterwards from below. Noise level and pressure loss remain constant in all air guide blade positions.

Slot diffuser made of extruded aluminium profiles in natural colour anodised E6/EV1 or painted to RAL 9010 (white).

Air guide element made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Volumetric flows in m³/h at:	35 dB(A)		40 dB(A):

DSX-XXL-P-1 				172			216

DSX-XXL-P-2				293			344

DSX-XXL-P-3 				425			498

DSX-XXL-P-4 				492			581

Product: SCHAKO type DSX-XXL-P-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	3 (3-slot)

-	4 (4-slot)

-	Air guide element position:

-	L II L, one-way horizontal throw on the left

-	L II R, one-way horizontal throw on the right

-	L III, alternately horizontal throw (standard)

-	Length:

-	500 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-		Return air version with air guiding blades

Product: SCHAKO type DSX-XXL-P-A

Accessories:

-	with galvanised sheet steel plenum box (-ASK), and lateral connection spigot and fixing lugs.

-	with a damper (-DK) in the plenum box adjustable on the front side for the air volume control

-	with rubber lip seal (-GD)

-	with thermal insulation

-		internal (-li)

-	external (-la)

-	with M4 riveting nuts

-	with end piece (-ES2) (supplied loose as standard)

-	made of anodised natural colour aluminium (E6/EV1)

-	aluminium painted in white (RAL 9010)

-	Corner bracket 90° (-EW) (supplied loose as standard)

Ceiling slot diffuser type DSX-XXL-PA, for supply air, with support profile for installation in ceiling panels, suitable for installation in closed ceiling systems. Air outflow direction can be adjusted afterwards from below. Noise level and pressure loss remain constant in all air guide blade positions.

Slot diffuser made of extruded aluminium profiles in natural colour anodised E6/EV1 or painted to RAL 9010 (white).

Air guide element made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Volumetric flows in m³/h at:	35 dB(A)		40 dB(A):

DSX-XXL-PA-1 			172			216

DSX-XXL-PA-2				293			344

DSX-XXL-PA-3 			425			498

DSX-XXL-PA-4 			492			581

Product: SCHAKO type DSX-XXL-PA-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	3 (3-slot)

-	4 (4-slot)

-	Air guide element position:

-	L II L, one-way horizontal throw on the left

-	L II R, one-way horizontal throw on the right

-	L III, alternately horizontal throw (standard)

-	Length:

-	500 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-		Return air version with air guiding blades

Product: SCHAKO type DSX-XXL-PA-A

Accessories:

-	with galvanised sheet steel plenum box (-ASK), and lateral connection spigot and fixing lugs.

-	with a throttle damper (-DK) in the connection spigot adjustable from the front for air volume regulation.

-	with rubber lip seal (-GD)

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	with M4 riveting nuts

-	Corner bracket 90° (-EW) (supplied loose as standard)

Ceiling slot diffuser type DSX-XLL-PB, for supply air, with support profile for installation in ceiling panels, suitable for installation in closed ceiling systems. Air outflow direction can be adjusted afterwards from below. Noise level and pressure loss remain constant in all air guide blade positions.

Slot diffuser made of extruded aluminium profiles in natural colour anodised E6/EV1 or painted to RAL 9010 (white).

Air guide element made of plastic, similar to RAL colour

-	9005 (black, -LS) (standard) or

-	9010 (white, -LW)

Volumetric flows in m³/h at:	35 dB(A)		40 dB(A):

DSX-XXL-PB-1 			172			216

DSX-XXL-PB-2				293			344

DSX-XXL-PB-3 			425			498

DSX-XXL-PB-4 			492			581

Product: SCHAKO type DSX-XXL-PB-Z

-	Model (number of slots)

-	1 (1-slot)

-	2 (2-slot)

-	3 (3-slot)

-	4 (4-slot)

-	Air guide element position:

-	L II L, one-way horizontal throw on the left

-	L II R, one-way horizontal throw on the right

-	L III, alternately horizontal throw (standard)

-	Length:

-	500 mm

-	1000 mm

-	1500 mm

-	in band design with plenum box (-ASK) and concealed mounting (-VM)

-	Model without plenum box

-	as dummy piece (-BS)

-	with M4 riveting nuts

-	for operation with overflow air with mounting bracket (pair) (-BW)

-	with M4 riveting nuts

-		Return air version with air guiding blades

Product: SCHAKO type DSX-XXL-PB-A

Accessories:

-	with galvanised sheet steel plenum box (-ASK), and lateral connection spigot and fixing lugs.

-	with a throttle damper (-DK) in the connection spigot adjustable from the front for air volume regulation.

-	with rubber lip seal (-GD)

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	with M4 riveting nuts

-	with end piece (-ES3) (supplied loose as standard)

-	Natural colour anodised aluminium (E6/EV1)

-	aluminium painted in white (RAL 9010)

-	Corner bracket 90° (-EW) (supplied loose as standard)