Ceiling Slot Diffuser DSXL

Specification texts

The ceiling slot diffuser DSXL is suitable for installation in closed ceiling systems, in rooms of heights 2.6 to 4 m. It can be used in cooling or heating mode by adjusting the air guide elements which can also be adjusted from below when installed. Free cross-section, resistance and noise level remain constant in all air guide element positions.

| Volumetric flows in m³/h per m at: | 35 dB(A) | 40 dB(A) |
| --- | --- | --- |
| DSXL-1 | 172 | 216 |
| DSXL-2 | 293 | 344 |
| DSXL-3 | 425 | 498 |
| DSXL-4 | 492 | 581 |

Supply air model with air guide elements.

Installation position of air guide elements:

-	air guide element position -B / -L / -R

Product: SCHAKO type DSXL-…-Z-…

Return air model with air guide elements.

Installation position of air guide elements:

-	air guide element position -L

Product: SCHAKO type DSXL-…-A-…

Model (number of slots):

-	1-slot (-1)

-	2-slot (-2)

-	3-slot (-3)

-	4-slot (-4)

Frame profile:

-	narrow frame profile, without support profile, for invisible installation (-S0, standard).

-	frame profile P0, with support profile, for visible installation (-P0).

-	frame profile PB, with support profile, for visible installation (-PB).

Frame surface:

-	Natural colour anodised aluminium (-ELOX, standard for DSXL-…-P0 and DSXL-…-PB models)

-	Painted aluminium (standard for DSXL-…-S0 model and painted to the same colour as blade colour of air guide element):

-	RAL 9005 (black) (-9005)

-	RAL 9010 (white) (-9010)

-	painted to a different RAL colour, freely selectable (at an extra charge) (-xxxx, always with 4 digits)

Blade colour (air guide element)

Air guide element made of plastic material:

-	Colour similar to RAL 9005 (black, standard) (-L9005).

-	Colour similar to RAL 9010 (white) (-L9010)

Blade position for air jet:

-	one-way horizontal throw on the left (-L, standard for return air)

-	one-way horizontal throw on the right (-R)

-	two-way horizontal throw (-B, standard for supply air)

Length / Model:

Single design (-N)

-	length L= 1000 mm (-N-01000)

-	length L= 1500 mm (-N-01500)

-	Length (L) in mm, freely selectable (-N-xxxxx) (always with 5 digits).

(in case of single design length L ≥ 400 mm to ≤ 1500 mm can be fitted with plenum box, dummy piece possible from length ≥ 200 mm).

Band design (-B)

-	Length (L) in mm, freely selectable, as band (-B-xxxxx) (always with 5 digits).

(Available lengths according to SCHAKO standard).

Single element length max. 1500 mm. With double air guide element (1x per connection) and connecting element, supplied loose. To lock the slot diffusers, double air guide elements are used at the butt joints (supplied loose, installation on site).

Mounting:

-	without connection (-00)

-	Slot diffuser is not connected to the plenum box

-	Standard with dummy piece (-BS) and with mounting bracket (-BW)

-	Concealed mounting with plenum box (-VM, standard)

-	Slot diffuser is connected to the plenum box ex works

-	The slot diffuser is screwed to the plenum box housing (face part) with concealed screws

-	Clamp strap (-KB)

-	Only possible without plenum box

-	Screws and clamp straps are supplied loose (pair)

-	Possible for the models DSXL-…-P0 and DSXL-…-PB

-	Not possible for model DSXL-…-S0

-	The slot diffuser is screwed to the clamp strap with concealed screws (included in delivery)

-	For mounting, access on the rear is not required!

-	Suspension via fastening holes

-	Model:

-   dummy piece design (-BS)

-   mounting bracket design (-BW, pair)

-	Only possible without plenum box

-	The slot diffuser is fastened to 4 suspension brackets

Accessories:

-	Plenum box (-ASK-22), made of galvanised sheet steel (-SV).

-	Model (number of slots):

-	1-slot (-1)

-	2-slot (-2)

-	3-slot (-3)

-	4-slot (-4)

-	Single / band design:

-	Single design (-N, length of box KL max. 1500 mm)

-	Band design (-B, available lengths according to SCHAKO standard for band design)

-	Length:

-	Length L = 1000 mm (-01000) (KL = 997 mm)

-	Length L = 1500 mm (-01500) (KL = 1497 mm)

-	Length (L/BL) in mm, freely selectable (-xxxxx, always with 5 digits) (length of box KL = L-3 / total length of box GKL = BL-3, can be fitted with a plenum box in case of single design lengths L = ≥ 400 mm to ≤ 1500 mm)

-	Mounting of box:

-	without connection (-00) (not connected to the slot diffuser, screws supplied loose)

-	concealed mounting (-VM, standard) (connected to the slot diffuser ex works)

-	Damper:

-	without damper (-DK0) (standard)

-	with damper made of galvanised sheet steel, adjustable, for simple air volume regulation:

-	in the plenum box housing (only with lateral spigot position [-S1/-S2]) (-DK1)

-	in the connection spigot, with cable-operated adjustment (with spigot position from above [-S0]) (-DK2)

-	Rubber lip seal:

-	without rubber lip seal (-GD0, standard)

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot

-	Insulation:

-	without insulation (-I0, standard)

-	with internal insulation (-Ii), thermal insulation inside the plenum box.

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	Standard height of plenum box (-KHS).

-	Height of box in mm, freely selectable (-xxx, always with 3 digits) (minimum height [GH] with spigot position S1+S2 and standard box neck = spigot diameter øD + 82 mm / with spigot position S0 = 180 mm).

-	Box neck

-	Standard box neck (KVS = 45 mm) (-KVS)

-	Box neck extension in mm, freely selectable (-xxx, always with 3 digits). Box neck (not adjustable) from ≥45 mm to 200 mm possible.

-	Spigot position:

-	spigot from above (-S0)

-	lateral spigot (-S1) (standard)

-	lateral spigot located on the opposite side (-S2)

-	Suspension with mounting brackets:

-	without riveting nut (-E0) (standard)

-	with riveting nut (-EM), made of brass

-	with air diffuser plate, made of galvanised sheet steel

-	Connection plate for band design (2x per butt joint), made of galvanised sheet steel. Number of suspension (without / with riveting nuts) per butt joint is reduced from 4x to 2x.

-	Corner angle (-EW-22), frame and dummy profile made of extruded aluminium profile. Firmly screwed to the connecting elements, made of galvanised sheet steel.

-	Model (number of slots):

-	1-slot (-1)

-	2-slot (-2)

-	3-slot (-3)

-	4-slot (-4)

-	Frame profile:

-	narrow frame profile, without support profile, for invisible installation, (-S0, standard)

-	frame profile P0, with support profile, for visible installation (-P0)

-	frame profile PB, with support profile, for visible installation (-PB)

-	Frame surface:

-	Natural colour anodised aluminium (-ELOX, standard for DSXL-…-P0 and DSXL-…-PB models)

-	Painted aluminium (standard for DSXL-…-S0 model and painted to the same colour as dummy profile / air guide element):

-	RAL 9005 (black) (-9005)

-	RAL 9010 (white) (-9010)

-	a freely selectable RAL colour (-xxxx, always with 4 digits)

-	Dummy profile colour (air guide elements)

-	Dummy profile made of painted aluminium:

-	colour similar to RAL 9005 (black) (-B9005) (standard)

-	colour similar to RAL 9010 (white) (-B9010)

-	a freely selectable RAL colour (-Bxxxx) (always with 5 digits)

-	Air guide elements (double), mounted ex works, made of plastic material similar to dummy profile colour.

-	Angle between sides:

-	angle  = 90° (-090) (standard)

-	angle () as required (-xxx), values between  = 90° (-090, standard) and 170° (-170) are possible (always with 3 digits)

-	Left-side length (a):

-	standard length L = 300 (-000)

-	length (L) in mm, freely selectable (-xxx) (minimum length = standard length) (always with 3 digits)

-	Right-side length (b):

-	standard length L = 300 (-000)

-	length (L) in mm, freely selectable (-xxx) (minimum length = standard length) (always with 3 digits)

-	End pieces (-E0 / -ES / -EB / -EL / -ER)

-	without end piece (-E0) (standard)

-	with end pieces:

-	supplied loose (-ES, pair) (standard)

-	mounted ex works on both sides (-EB)

-	mounted ex works on the left side (-EL)

-	mounted ex works on the right side (-ER)

made of aluminium (same colour as frame)

-    Mounting bracket (pair) / dummy piece (-B0 / -BW / -BS)

-	without mounting bracket / without dummy piece (-B0)

-	with mounting bracket (-BW), for overflow operation:

-    made of galvanised sheet steel

-    only possible without plenum box

-    possible from length L ≥ 200 mm

-	with dummy piece (-BS):

-    made of galvanised sheet steel

-    only possible without plenum box

-    possible from length L ≥ 200 mm

With models -BW and -BS as a band, additional connecting fishplates are supplied loose.