Floor slot diffuser FBS

Specification text

Floor slot diffuser type FBS for installation in double floors for installation in the facade area. High vertical penetration at high T. Supply air jet is spread over a large area with high-speed reduction of temperature and speed in the occupied area down to the floor level. Suitable for conference rooms. The floor slot diffuser type FBS-AU achieves very high sound absorption values.

It consists of slot diffuser FDSXW (-70), 1-slot, with wide frame profile (-PB), with integrated cross-talk sound attenuator box with round connection spigot. Sound-absorbing

box made of galvanised sheet steel with abrasion-resistant absorption material attached on both sides with fastening system for mounting. Slot rail consisting of frame profile made of aluminium natural colour anodised (E6/EV1) or aluminium painted to RAL 9010 (white), including insulating strips, with integrated dirt collection basket and end pieces on both sides. Blades made of plastic, similar to RAL colour 9005 (-L9005, black) or RAL 9010 (-L9010, white). Fastening by means of fastening prongs.

Make: SCHAKO type FBS-AU

Consisting of slot diffuser FDSXW (-70), 1-slot, with wide frame profile (-PB), with integrated hit-and-miss damper made of galvanised sheet steel. Slot rail consisting of frame profile made of aluminium natural colour anodised (E6/EV1) or aluminium painted to RAL 9010 (white), including insulating strips, with integrated dirt collection basket and end pieces on both sides. Blades made of plastic, similar to RAL colour 9005 (-L9005, black) or RAL 9010 (-L9010, white). Fastening by means of fastening prongs. Including casting core for casting the floor screed, made of styropor.

Product: SCHAKO type FBS-SS

Accessories:

-	Damper (-DK2), manually adjustable through cable, consisting of damper made of galvanised sheet steel and damper fastening made of plastic (FBS-AU only).

-	Corner bracket 90° (-EW) (supplied loose as standard)

-	Rubber lip seal (-GD1), made of special rubber

(FBS-AU only)

-	Cover (-OA1), made of galvanised sheet steel

-	Dummy box (-BLK) as connecting element for optic design, made of galvanised sheet steel.

-	Pressure measurement box for easy measurement of the supply air volumetric flow from outside, made of galvanised sheet steel.