Grease Trap Grille FG

Specification texts

Grease trap grille for ceiling mounting, consisting of frame and grease trap collector made of natural colour anodized aluminium (-AL-ELOX), sheet steel painted to RAL 9010 (white, -SB-9010) or sheet steel painted to a freely selected RAL colour (-SB-xxxx). With inserted, replaceable grease trap blades made of aluminium (-L) or with inserted, replaceable grease collection mat made of woven aluminium (15 mm, -M).

Easy to disassemble for cleaning purposes by turning the sash locks.

Product: SCHAKO type FG-D

-	for wall mounting

Product: SCHAKO type FG-W

Fastening:

-	With screw mounting (-SM, standard)

Accessories:

-	Plenum box (-AK-...-N-...), in rectangular design, for single length.

-	Housing with round connection spigot and fixing lugs consisting of:

-	Galvanised sheet steel (-SV, standard)

-	Fastening:

-	Screw mounting (-SM, standard)

-	Height of plenum box standard (-KHS) or freely selectable (-xxx, in mm) (minimum height with spigot position -S1 / -S4

= spigot diameter 87 mm)

-	Width of plenum box: standard (-KBS) or freely selectable (-xxx in mm) (minimum width with spigot position -S0 / -S4

= spigot diameter øD + 30 mm)

-	Spigot diameter: standard (-SDS) or freely selectable (-xxx, in mm)

-	Spigot position:

-	1 spigot from above (-S0)

-	1 lateral spigot on the box (-S1, standard)

-	1 spigot front side (-S4)

-	with damper (-DK1) in plenum box, adjustable, for simple air volume regulation. Consisting of electrolytically galvanised sheet steel. plastic damper fixing

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with thermal insulation:

-	internal (-li), inside the plenum box

-	external (-Ia), at the outside of the plenum box

-	Installation frame (-ER1 / -ER2), comprising electrolytically galvanised sheet steel (not available in connection with plenum box).

-	without wall anchor (-ER1), (standard)

-	with wall anchor (-ER2) (only at an extra charge)