Lint sepatator FLAQ

Specification texts

Lint separator for filtering textile fibre charged return air from clean rooms, consisting of a square frame and a fitted, replaceable lint separator insert made of sheet steel painted to RAL 9010 (white) (-PS-9010), sheet steel painted to RAL colour which can be freely selected (-PS-xxxx) or stainless steel 1.4301 (V2A) sand silver painted (-V2-SAND), with back-fitted wire fabric made of stainless steel 1.4301 (V2A), mesh width 0.8 mm x 0.5 mm.

For cleaning and disinfection purposes, easy to disassemble by turning the sash lock.

Product: SCHAKO type FLAQ-...

Fastening:

-	With screw mounting (-SM, standard)

-	with concealed mounting (-VM) (only possible in connection with an installation frame or a plenum box)

Accessories:

-	Plenum box (SK-Q-19-...-A-...), for square air diffusers.

-	Housing with round connection spigot and fixing lugs consisting of:

-	Sheet steel (-SB), painted inside and outside to RAL 9010 (white)

-	Stainless steel V2A (-V2)

-	Model for return air (-A)

-	Fastening:

-	Screw mounting (-SM, standard)

-	Concealed mounting (-VM), additionally with pole brace made of aluminium and pole brace holder 			made of plastic.

-	Height of plenum box: standard (-KHS) or freely selectable (-xxx, in mm) (minimum height with spigot 		position -S1 / -S2 / -S3 / -S5 =  spigot diameter øD + 102 mm, but at least 200 mm)

-	Spigot diameter: standard (-SDS) or freely selectable (-xxx, in mm).

-	Spigot position:

-	Spigot from above (-S0)

-	1 lateral spigot (-S1) (standard)

-	2 lateral spigots, offset by 90° (-S2)

-	2 lateral spigots, offset by 180° (-S3)

-	2 spigots arranged next to each other (-S5)

-	with damper (-DK1) in plenum box, adjustable, for simple air volume regulation. Consisting of 			electrolytically galvanised sheet steel. plastic damper fixing

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with volumetric flow meter (-VME1). (not for use with a damper)

-	with ROB version (-ROB1), removable damper and volumetric flow meter.

-	with thermal insulation:

-	internal (-li), inside the plenum box

-	external (-Ia), at the outside of the plenum box

-	Installation frame (-ER1 / -ER2), comprising electrolytically galvanised sheet steel (not available in 	connection with plenum box).

-	without wall anchor (-ER1), (standard)

-	with wall anchor (-ER2) (only at an extra charge)