Ventilation Grille Ib-R

Specification texts

Ventilation grille type IB-R-... for supply and return air, for installation in sheet metal / spiral ducts, with horizontal or vertical, pivoting, individually adjustable air deflection blades on the front side. For description of frames and blades, see “Material / paint”. Assembly parts made of electrolytically galvanised sheet steel.

In single design. With screw mounting (-SM, standard), screws must be provided on site. Without installation frame.

Product: SCHAKO type IB-R-...-N-...-SM-ER0

Blades (design):

-	horizontal, pivoting air deflection blades on the front side (-IB-R-01-…).

-	same as IB-R-01-…, additionally with hit-and-miss damper (-IB-R-08-…).

-	same as IB-R-01-…, additionally with vertical, pivoting air deflection blades and hit-and-miss damper 	(-IB-R-8c-…).

-	vertical, pivoting air deflection blades on the front side

(-IB-R-10-…).

-	same as IB-R-10-…, additionally with hit-and-miss damper (-IB-R-15-…).

-	same as IB-R-10-…, additionally with horizontal, pivoting air deflection blades and hit-and-miss damper 	(-IB-R-16-…).

Length:

-	315 mm (-0315)

-	415 mm (-0415)

-	515 mm (-0515)

-	615 mm (-0615)

-	815 mm (-0815)

-	1015 mm (-1015)

-	1215 mm (-1215)

Height:

-	65 mm (-065)

-	115 mm (-115)

-	215 mm (-215)

Air throw pattern:

-	blade position straight (-L000, standard).

-	blade position 44° diverging (-L044).

-	blade position 84° diverging (-L084).

-	blade position 110° diverging (only for IB-R-10 / IB-R-15 / IB-R-16) (-L110).

-	blade position 140° diverging (only for IB-R-10 / IB-R-15 / IB-R-16) (-L140).

-	blade position opposite to one another (-LGEG).

Material / paint (frames and blades):

-	Galvanised sheet steel (-SV) (standard).

-	Sheet steel (-SB):

-	painted to the colour RAL 9010 (white) (-9010).

-	painted to a RAL colour of your choice (-xxxx, at an extra charge).