Ceiling Diffuser IDA

Specification text

The ceiling diffuser IDA for cooling and heating large and high halls is specially designed for installation flush

with the ceiling, in order to comply with spatial and architectural demands.

In order to prevent draughts in the cooling mode, the supply air must largely be discharged horizontally from

the diffuser. However, in the heating mode, the diffuser must have high penetration depth, in order to

achieve fast and efficient heating. The ceiling diffuser type IDA with manually adjustable air guide funnel and

square faceplate meets both these requirements ideally. Suitable for installation heights ranging from 3 m to

10 m maximum. Diffuser consisting entirely of sheet steel painted with a high-quality powder coating to a

RAL colour (RAL 9010 (white), standard). It is fastened by concealed mounting (-VM) using a central

fastening screw.

Product: SCHAKO type IDA-Q-ZH-.../ IDA-Q-ZV-...

-	Return air model without air guide funnel

Product: SCHAKO type IDA-Q-AA-...

-	Supply air model with round faceplate and air guide funnel

Product: SCHAKO type IDA-R-ZH-.../ IDA-R-ZV-...

-	Return air model with round faceplate without air guide funnel

Product: SCHAKO type IDA-R-AA-...

-	with screw mounting (-SM) (IDA-Q only), only for model with ball-impact guard

-	with screw mounting with concealed mounting (-VS), only for model with ball-impact guard (-BS) (only for NW 800)

Accessories:

-	Plenum box (SK-Q-08 and SK-R-08), made of galvanised sheet steel, inside painted to RAL9005 (black), with fixing lugs, with air diffuser plate (for supply air model only)

-	with damper (-DK1) in the connection spigot Damper made of galvanised sheet steel

-	adjustable with cable (-DK2)

-	with volumetric flow meter (-VME, available for IDA up to NW625)

-	with ROB version (-ROB1), removable damper and volumetric flow meter (only SK-Q)

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	Height of plenum box can be freely selected, xxx in mm, minimum height = spigot diameter +147 mm, 	but at least 245 mm.

-	Spigot diameter can be freely selected, xxx in mm

-	Spigot position:

-	S0= spigot from above

-	S1 = lateral spigot on the box (standard)

-	S2= 2 spigots offset by 90°

-	S3= 2 spigots offset by 180°

-	S5= 2 spigots arranged next to each other

-	with electric actuator (3-point activation)

-	24 V AC (standard)

-	without auxiliary switch (-E090)

-	with 2 integrated auxiliary switches (-E093)

-	230 V AC (-E092)

-	Thermocouple adjustment (-TE01) diffuser adjustment option without electrical energy as a function of the supply air temperature (heating mode > 26°C, cooling mode < 26°C).

-	Ball-impact guard (-BS), made of steel painted to RAL 9010 (white), other RAL colours possible at an extra charge (possible only for IDA-Q-... with screw mounting and for NW 800 only with concealed mounting). Attention: With reduced drill pattern, only possible with plenum box in the same size as the faceplate.