Diffuser for large air volumes IGA

SPECIFICATION TEXT

The SCHAKO air diffuser IGA for large air volumes for use in supply and return air systems.

The SCHAKO air diffuser IGA for large air volumes is suitable for use in supply and return air systems for air-conditioning of large rooms with heights of up to 15 m. The air diffuser is connected directly to the duct system and is suitable for VAV systems with variable volumetric flows of 40-100%.

The air diffuser is adjustable by motor as standard and can be used for both cooling and heating. In cooling mode, a very high induction is achieved, which effectively reduces the air velocity and temperature. The motorised changeover to heating mode produces a very compact, vertical air jet which ensures a high penetration depth even at large installation heights at high overtemperature.

The air diffuser IGA for large air volumes consists of several inlet funnels for the optimum discharge of supply air in cooling and heating mode.

The air diffuser IGA consists of a painted faceplate made of sheet steel. With outer and inner inlet nozzle made of aluminium painted to the colour of the faceplate. Connection via spigot made of galvanised sheet steel.

Supply air model with internal air volume regulator made of aluminium (painted to the colour of the faceplate) including electrical regulator and height-adjustable baffle plate. Baffle plate position: top for heating mode / bottom for cooling mode.

Product: SCHAKO type IGA-...-Z

Return air model without air volume regulator and baffle plate

Product: SCHAKO type IGA-...-A

Paint (faceplate):

-	RAL colour 9010 (white) (-9010) (standard).

-	RAL colour can be freely selected (-xxxx) (always with 4 digits).

Actuator (standard for supply air):

-	without actuator (-E000) (standard for return air).

-	with actuator 24 V AC/DC, 2/3-point

- 	IGA-500 (-E085)

- 	IGA-630 / IGA-800 (-E086)

-	with actuator 230 V AC, 2/3-point

- 	IGA-500 (-E083)

- 	IGA-630 / IGA-800 (-E084)

Accessories:

--	Damper:

-	without damper (-DV0) (standard).

--	with adjustable damper, for air volume regulation, with side adjustment lever, made of galvanised sheet steel, painted to the IGA colour on the outside:

-	connection without rubber lip seal (-DV1) (standard for model with damper).

-	connection with rubber lip seal (-DV3), made of special rubber.

--	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.