Ideal Comfort Diffuser IKA

Specification text

Ideal comfort diffuser particularly suitable for optimum cooling and heating of large and high rooms and halls. High-induction supply air intake in cooling mode by splitting the horizontal, radial supply air jet into several smaller jets due to reduction in temperature. Compact vertical round jet in heating mode with great penetration for effective heating. Flexible air supply by continuous manual adjustment from only horizontal to only vertical throw without any change in the pressure loss and sound power level. Possible installation as a free suspension or at the ceiling. Simple integration in the duct system via round connection piece. Round design with outer diffuser casing and adjustable inner basket to change air flow direction. Only a short inflow distance necessary due to built-in perforated air flow straightener. Diffuser consisting entirely of sheet steel painted with a high-quality powder coating to a RAL colour RAL 9010 (white, standard), RAL 9006 (white aluminium) or to a different RAL colour (at an extra charge).

Product: SCHAKO type IKA		-...

Accessories:

-	Rubber lip seal (-GD1), made of special rubber for connection to a spiral duct

-	With round plenum box (-AKR) made of galvanised sheet steel with fixing lugs

-	With a damper (-DK1) adjustable from the room side in the plenum box for simple air volume 					regulation.

-	with rubber lip seal (-GD1), made of special rubber.

-	with thermal insulation

-	internal (-Ii)

-	external (-Ia)

-	with ball-impact guard (-BS...), steel powder-coated in the colour of the diffuser.

-	Fastened to the diffuser (standard) (-BSA)

-	Fastened to the ceiling (-BSD)

-	With damper (-DV1/-DV2/-DV3), made of galvanised sheet steel, integrated, room side adjustable for 	simple volumetric flow adjustment.

-	Connection to spiral duct (-DV1)

-	Connection to connection pieces (-DV2)

-	Connection to spiral duct with rubber lip seal (-DV3)

-	with electric actuator (-ME) for adjusting air jet direction. For NW 400-800 integrated on the inside, for NW 	300 on the outside. NW 300 and 800 with  Belimo actuator. NW 400 to 600 with Siemens actuator

Model

-	230 V AC, 3-point activation (-E045, -E092, -E006)

-	24 V AC, 0 - 10 V DC (-E046, -E091, -E014)

-	24 V AC, 3-point activation (-E044, -E090, -E005)

-	Thermocouple (-TE01, only possible for NW 600),

Diffuser adjustment option without electrical energy as a function of the supply air temperature (not 			available in connection with damper)