Compact Filter Grille KG-F

Specification texts

Compact filter grille type KGF-Q-08-... for supply and return air, for installation in rectangular ductwork. This model consists of a front frame with visible screw mounting (SM), with pivoting horizontal air deflection blades and integrated hit-and-miss damper for air volume regulation. With integrated filter insert ISO Coarse > 45% (dry layer filter mat). Blade insert removable from the front side.

Product: SCHAKO type KGF-Q-08-...

-	Compact filter grille made of

-	Galvanised sheet steel

-	Galvanised sheet steel, front side painted to RAL colour 9010 (white)

Accessories:

-	With plenum box (-AK) made of galvanised sheet steel

-	With rubber lip seal (-GD1) at the connection spigot

-	with thermal insulation

- internal (-li)

- external (-la)

-	with cover frame (-BR), for concealed mounting (VM), made of

-	aluminium natural colour anodised E6/EV1

-	aluminium painted to RAL colour 9010 (white)

Compact filter grille type KGF-R-08-... for supply and return air, for installation in sheet metal / spiral ductwork. This model consists of a front frame with visible screw mounting (SM), with pivoting horizontal air deflection blades and integrated hit-and-miss damper for air volume regulation. With integrated filter insert ISO Coarse > 45% (dry layer filter mat). Blade insert removable from the front side.

Product: SCHAKO type KGF-R-08-...

-	Compact filter grille made of

-	Galvanised sheet steel

-	Galvanised sheet steel, front side painted to RAL colour 9010 (white)