Round duct compact grille type KGRR

Specification texts

Round duct compact grille KGRR for supply and return air suitable for connection to DIN ducts. With integrated, manually adjustable hit-and-miss damper made of galvanised sheet steel, for simple air volume and ductwork regulation.

-	With horizontal front side adjustable air deflection blades.

Product: SCHAKO type KGRR-08-...

-	With vertical front side adjustable air deflection blades.

Product: SCHAKO type KGRR-15-...

-	Nominal width

200 mm (-200)

224 mm (-224)

250 mm (-250)

280 mm (-280)

315 mm (-315)

355 mm (-355)

400 mm (-400)

450 mm (-450)

500 mm (-500)

560 mm (-560)

630 mm (-630)

-	Length

-	1-part: 500 / 750 / 1000 (-0500/-0750/-1000)

-	2-part: 1500 / 1750 / 2000 (-1500/-1750/-2000)

-	Grille height

-	65 (-065)

-	115 (-115)

-	215 (-215)

-	315 (-315)

-	Air throw pattern

-	Blade position straight (-L000) (standard).

-	Horizontal blade position, one-way right (L00R) (KGRR-08-... only).

-	Horizontal blade position, one-way left (-L00L) (KGRR-08-... only).

-	Blade position 44° diverging (-L044).

-	Blade position 84° diverging (-L084).

-	Blade position opposite to one another (-LGEG)

-	Material and paint (round duct):

-	Galvanised sheet steel (-SV-0000) (at an extra charge).

-	Sheet steel painted to RAL 9010 (white) (standard, -SB-9010).

-	Sheet steel painted to a freely selectable RAL colour (-SB-xxxx) (colour always with 4 digits).

-	Mounting position

-	3 o'clock (-3U)

-	6 o'clock (-6U, standard)

-	9 o'clock (-9U)

-	12 o'clock (-0U)

-	Fastening methods:

-	fastening hole

-	without fastening hole (-B0)

-	With fastening hole ø11.5 mm (-BB, standard).								(Prepared for suspended installation by using an M8 threaded rod and an M8 nut 			to be provided on site).

Accessories (at an extra charge):

-	Rubber lip seal (-GD0/-GD1)

-	without rubber lip seal (-GD0, standard).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

For more accessories, please refer to the separate documentation "Round duct system accessories".