Ceiling return air diffuser type LAQ

Specification texts

Perforated return air diffuser for use in return air systems. The diffusor is suitable for extraction of the room exhaust air. The ceiling return air diffuser is suitable for VVS systems with variable volumetric flows.

-	Permanently mounted diffuser, with perforated faceplate made of sheet steel (-SB) painted to RAL 9010 (white, -9010) or to another freely selectable RAL colour (-xxxx). With clip mounting (-KM, non-detachable).

Not available or not suitable for use with filter mat.

Product: SCHAKO type LAQ-F-...

-	Removable diffuser, with perforated faceplate made of sheet steel (-SB) painted to RAL 9010

(white, -9010) or to another freely selectable RAL colour (-xxxx). With concealed mounting (-VM), via central screw.

Can optionally be delivered with filter mat (ISO Coarse 25% - ISO Coarse > 45%).

Product: SCHAKO type LAQ-E-...

-	Hinged diffuser, with perforated faceplate hinged on one side (click system), made of sheet steel (-SB) painted to RAL 9010 (white, -9010) or to another freely selectable RAL colour (-xxxx). Front frame made of extruded aluminium profiles in natural colour anodised (E6/EV1), painted to RAL 9010 (white, -9010) or to another freely selectable RAL colour (-xxxx). Front frame fastened via central screw (concealed mounting -VM).

Can optionally be delivered with filter mat (ISO Coarse 25% - ISO Coarse >45%).

Product: SCHAKO type LAQ-K-...

Nominal size: NW 310 to NW 625

Due to the function, the ceiling return air diffuser LAQ is only available with plenum box.

Accessories:

Filter mat:

-	without filter mat (-G0, standard) (LAQ-F only available without filter mat)

-	with filter mat, made of synthetic fibres (fibre fleece with non-breaking fibres):

-	filter class ISO Coarse 25% - 35% (-G2)

-	filter class ISO Coarse 35% - 45% (-G3)

-	filter class ISO Coarse > 45% (-G4)

Plenum box (-SK-Q-...), square design, made of galvanised sheet steel (-SV, standard), inside painted to RAL colour 9005 (black), with fixing lugs, in the nominal sizes NW 310 to 625.

--	Air diffuser:

-	suitable for LAQ-F (-20).

-	suitable for LAQ-E (-04).

-	suitable for LAQ-K (-59).

--	Type of air: return air (-A).

--	Fastening:

-	concealed mounting (-VM) (only available for LAQ-E and LAQ-K).

-	clip mounting (-KM) (only available for LAQ-F). The ceiling air diffuser is permanently fastened to the

plenum box with steel clips.

--	Damper:

-	without damper (-DK0) (standard).

-	with damper (-DK1), made of galvanised sheet steel, in the plenum box housing, adjustable, for simple

air volume regulation.

-	with damper (-DK2), same as DK1 but with cable-operated adjustment, with spigot position from

above only (-S0) (not possible for LAQ-F)

--	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.

--	Volumetric flow meter:

-	Without volumetric flow meter (-VME0) (standard).

-	With volumetric flow meter (-VME1), holder made of galvanised sheet steel, measuring sensor made

of plastic, connections made of aluminium.

--	ROB version:

-	Without ROB version (-ROB0) (standard).

–	With ROB version (-ROB1). Removable diffuser plate, damper and volumetric flow meter

(not possible for LAQ-F).

--	Insulation:

-	Without insulation (-I0)

-	with internal insulation (-Ii), thermal insulation inside the plenum box.

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

--	Height of plenum box:

-	Standard height of plenum box (-KHS).

-	Height of plenum box in mm, can be freely selected (-xxx) (minimum height [KHS] with spigot position

S1 / S2 / S3 / S5 = spigot diameter + 102 mm, but at least 200 mm, minimum height [KHS] with spigot

position S0 at least 200 mm) (always with 3 digits).

--	Spigot diameter:

-	Standard spigot diameter (-SDS).

-	Spigot diameter in mm, freely selectable (-xxx) (always with 3 digits).

--	Spigot position:

-	Spigot from above (-S0).

-	1 lateral spigot on the box (-S1) (standard).

-	2 lateral spigots, offset by 90° (-S2).

-	2 lateral spigots, offset by 180° (-S3).

-	2 spigots arranged next to each other (-S5).