Mixing Box Model MBE / MBP

Specification texts

Mixing box for use in twin-duct air-conditioning systems, for spiral duct connection to DIN 24 145 with integrated volumetric flow controller for use in constant and variable volumetric flow, room and duct pressure regulation. With positive control Vmin, Vmax or "CLOSED".

Consisting of a housing made of galvanised sheet steel lined with mineral wool, with a guide baffle made of perforated galvanised sheet steel. Housing containing two volumetric flow controllers, consisting of a round connection piece made of galvanised sheet steel with damper leaf made of galvanised sheet steel and silicone-free damper leaf seal for airtight design to DIN EN 1751, Class 2 (NW100 only), Class 3 (NW125 - 400 only), with measuring cross blades made of extruded aluminium profile, blade mount made of plastic (PA6). A special measuring cross allows position-independent mounting.

With electric control, control voltage 24 V AC, 50 / 60 Hz, temperature compensation of 10-40°C, wired and adjusted in-factory.

Product: SCHAKO type MBE

-	With pneumatic control

Feed pressure 1.2  ± 0.1 bar

-	Depressurised "CLOSED"

-	Depressurised "OPEN"

Temperature compensation of 0 - 50° C

Product: SCHAKO type MBP

Model

-	Cold air right (-KR), in air flow direction

-	Cold air left (-KL) in air flow direction (standard)

Accessories (at an extra charge):

-	Acoustic cladding (-DS) for reducing the radiated noise made of insulating material with sheet metal casing made of galvanised sheet steel.

-	Galvanised sheet steel connection frame (-AR).

-	Additional silencer (-ZS) made of galvanised sheet steel and baffle with mineral wool lining (MWK) and optionally with perforated sheet cover (MLK).

-	Rubber lip seal (-GD), made of special rubber.