Ceiling slot diffuser for small air volumes MINODSX

Specification text

The slot diffuser MINODSX is suitable for installation in closed ceiling systems, in rooms of heights 2.6 to 4.0 m. Pro-per insertion of the air guide elements allows the diffuser to be used in cooling or heating mode. The high induction ensures fast reduction of the air outflow velocity and of the temperature difference in the cooling mode. In the heating mode, the vertical air throw ensures a high penetration depth. In doing so, the free cross-section always remains constant. Likewise, the pressure loss and noise level do not change. A subsequent adjustment of the air jet pattern is not possible.

The slot diffuser consisting of faceplate with air guide elements and plenum box in rectangular design. Faceplate made of sheet steel. Plenum box with lateral round connection spigot and mounting brackets made of galvanised sheet steel. The faceplate is fastened on the plenum box using magnetic fastening.

Make:	SCHAKO type MINODSX

Model:

-	Size 1 (-1)

-	Size 2 (-2)

Paint (faceplate):

-	Sheet steel:

-	painted to RAL colour 9010 (white, standard) (-F9010).

-	painted to a different RAL colour, freely selectable

(-Fxxxx) (always with 5 digits).

Blade colour (air guide element)

-	Air guide element made of plastic:

-	similar to RAL colour 9005 (black) (-L9005).

-	similar to RAL 9010 (white, standard) (-L9010).

Blade position for air jet:

-	vertical throw (-V)

-	one-way horizontal throw to the right (-R)

-	one-way horizontal throw to the left (-L) (standard)

Accessories:

-	Damper:

-	without damper (-DK0) (standard).

-	with damper (-DK1), made of galvanised sheet steel, in the plenum box housing, adjustable, for simple 		air volume regulation.

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1) made of special rubber, at the connection spigot.

-	Universal fastening:

-	Without fastening (-B0)

-	with universal fastening (-BU)