Volumetric flow controller measuring cross MKAR / MKAQ

Specification texts

Volumetric flow measuring cross in round design, for use in supply and return air systems, for constant or variable volumetric flows. Allowed differential pressure range: 50-1000 Pa. Allowed ambient temperatures:

0 - 55°C Housing consisting of galvanised sheet steel, measuring cross made of extruded aluminium profile and measuring cross support made of plastic PA6. Special measuring cross allows position-independent installation.

Product: SCHAKO type MKAR

-	Housing made of:

-	Galvanised sheet steel (-SV)

-	galvanised sheet steel with DD coating (-DD)

-	Stainless steel 1.4571 (-V2)

-	Plastic PPs, measuring cross made of extruded aluminium profile and measuring cross support made of plastic PP (-KU)

Accessories:

-	Electric controller (-MExx)

Control voltage 24 V AC 50/60 Hz wired ex works The 0-10 V DC output signal can be used for actual

value display (corresponding to 0-100 % of the set volumetric flow Vnenn) in DDC/ZLT systems.		-	Metu flanges (-MF1), on both sides, type AF (-SV / -V2 only)

-	Flat flanges (-FF1), on both sides, according to DIN 24154/5, for model (-SV)

-	Flat flanges (-FF2), on both sides, according to DIN 24154/5, for model (-V2)

-	Flat flanges (-FF1), on both sides, according to DIN 24154/5, for model (-KU)

-	Rubber lip seal (-GD1) made of special rubber (-SV / -V2 only)

Volumetric flow measuring cross in rectangular design, for use in supply and return air systems, for constant or variable volumetric flows. Allowed differential pressure range: 50-1000 Pa. Allowed ambient temperatures: 0 - 55°C Housing consisting of galvanised sheet steel, measuring cross made of extruded aluminium profile and measuring cross support made of plastic PA6. Special measuring cross allows position-independent installation.

Product: SCHAKO type MKAQ

-	Housing made of:

-	Galvanised sheet steel (-SV)

-	galvanised sheet steel with DD coating (-DD)

-	Stainless steel to DIN 1.4571 (-V4A)

Accessories:

-	With electric controller (-MExx),

Control voltage 24 V AC 50/60 Hz wired ex works The 0-10 V DC output signal can be used for

actual value display (which corresponds to 0-100 % of the set air volume Vmax) in DDC/ZLT systems.