Mineral Wool Silencer Models MWS / MWK

Specification texts

Silencing baffles with frame profile in nozzle design for substantial reduction of the pressure loss. The mineral fibre boards, weight per unit volume > 30 kg/m³, are covered with unmetabolisable glass silk and are non-flammable according to DIN EN 13501-1 class 1. The baffle frame is made of galvanised sheet steel.

Baffles measured according to DIN EN ISO 7235. Manufactured according to the hygienic standards of VDI 6022-1.

Product: SCHAKO type MWK-OB-100/-200

Silencing baffles with frame profile in nozzle design for substantial reduction of the pressure loss. The mineral fibre boards, weight per unit volume > 30 kg/m³, are covered with unmetabolisable glass silk and are non-flammable according to DIN EN 13501-1 class 1. Covered with resonance plate offset on one side. The baffle frame and sectioned sheet are made of galvanised sheet steel.

Baffles measured according to DIN EN ISO 7235. Manufactured according to the hygienic standards of VDI 6022-1.

Product: SCHAKO type MWK-MB-100/-200

Silencing baffles with frame profile in nozzle design for substantial reduction of the pressure loss. The mineral fibre boards, weight per unit volume > 30 kg/m³, are covered with unmetabolisable glass silk and are non-flammable according to DIN EN 13501-1 class 1. Both sides covered with a perforated plate. The baffle frame and perforated sheet are made of galvanised sheet steel.

Baffles measured according to DIN EN ISO 7235. Manufactured according to the hygienic standards of VDI 6022-1.

Product: SCHAKO type MWK-LL-100/-200

Silencing baffles with frame profile in nozzle design for substantial reduction of the pressure loss. The mineral fibre boards, weight per unit volume > 30 kg/m³, are covered with unmetabolisable glass silk and are non-flammable according to DIN EN 13501-1 class 1. With resonance plate and perforated plate cover offset on one side. The baffle frame, sectioned sheet and perforated sheet are made of galvanised sheet steel.

Baffles measured according to DIN EN ISO 7235. Manufactured according to the hygienic standards of VDI 6022-1.

Product: SCHAKO type MWK-LB-100/-200

Material:

-	Galvanised sheet steel (standard) (-SV)

Baffle silencer with integrated baffles type MWS-OB-... with frame profile in nozzle design and with mineral fibre boards covered with unmetabolisable glass silk - weight per unit volume > 30 kg/m³, non-flammable according to EN 13501-1 class 1.

Duct housing made of galvanised sheet steel with airtight saddle joint. Airtightness class C according to DIN EN 15727, internal pressure up to max. 1000 Pa.

Flange profile M3 on both sides. Manufactured according to the hygienic standards of VDI 6022-1. The baffle frame is made of galvanised sheet steel.

Product: SCHAKO type MWS-OB-100/-200

Baffle silencer, with integrated baffles type MWS-MB-...  with frame profile in nozzle design and with mineral fibre boards covered with unmetabolisable glass silk - weight per unit volume > 30 kg/m³, non-flammable according to DIN EN 13501-1 class 1. Duct housing made of galvanised sheet steel with airtight saddle joint. Airtightness class C according to DIN EN 15727, internal pressure up to max. 1000 Pa.

Flange profile M3 on both sides. Manufactured according to the hygienic standards of VDI 6022-1. The baffle frame and sectioned sheet are made of galvanised sheet steel.

Product: SCHAKO type MWS-MB-100/-200

Baffle silencer, with integrated baffles type MWS-LL-...  with frame profile in nozzle design and with mineral fibre boards covered with unmetabolisable glass silk - weight per unit volume > 30 kg/m³, non-flammable.

Duct housing made of galvanised sheet steel with airtight saddle joint. Airtightness class C according to DIN EN 15727, internal pressure up to max. 1000 Pa.

Flange profile M3 on both sides. Manufactured according to the hygienic standards of VDI 6022-1. The baffle frame and perforated plate are made of galvanised sheet steel.

Product: SCHAKO type MWS-LL-100/-200

Baffle silencer with integrated baffles type MWS-LB-... with frame profile in nozzle design and with mineral fibre boards covered with unmetabolisable glass silk - weight per unit volume > 30 kg/m³, non-flammable according to EN 13501-1 class 1.

Duct housing made of galvanised sheet steel with airtight saddle joint. Airtightness class C according to DIN EN 15727, internal pressure up to max. 1000 Pa.

Flange profile M3 on both sides. Manufactured according to the hygienic standards of VDI 6022-1. The baffle frame, sectioned sheet and perforated plate are made of galvanised sheet steel.

Product: SCHAKO type MWS-LB-100/-200

Material:

-	Galvanised sheet steel (standard) (-SV)

Accessories:

-	Flange profile M2/ M4 (-M2/-M4)